## Slide 1: Performance Measurement Using Simple TWAMP for Segment Routing Networks
draft-gandhi-spring-stamp-srpm-04
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
Summary of Procedure
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay as well as Synthetic Loss and Direct Measurement
    Links and End-to-end P2P/P2MP SR Paths
      Links include physical, virtual, LAG (bundle), LAG member, numbered/unnumbered links
    Applicable to SR-MPLS/SRv6 data planes
  Handle ECMP for SR paths
Goals:
  Eliminate per session provisioning on Session-Reflector
  No control-channel signaling for sessions
  Scope:
  STAMP [RFC 8762]
  STAMP TLVs [draft-ietf-ippm-stamp-option-tlv]
  draft-gandhi-ippm-stamp-srpm

## Slide 4: Review Comments
Add references for well-known terms “link”, “SR path”. Reword “Congruent paths”
Destination UDP port used has zero UDP checksum for IPv6 header
  Add Reference for RFC 6936 in Security Section
  For IPv4 and IPv6 packets, where the hardware is not capable of re-computing the UDP checksum or adding checksum complement [RFC7820], the sender node MAY set the UDP checksum to 0 [RFC8085] and reflector node MAY accept it as long as it meets requirements specified in [RFC6936]
Add reference for Yang data model draft in provisioning model section
Liveness is to compute “connection loss” performance metric
Editorial
  Indicate packet loss is direct measurement
  Use test packet term, Sender as Session-Sender, Reflector as Session-Reflector
  H/W timestamps required -> H/W timestamps recommended
  IPv6 address ::1/128 or ::FFFF:127/104
  Clarify - Section 4.1.4.2 and 4.2.2.2 depict the test packet format with word “as needed” for inner IP Header
  UDP destination port when running authenticated and unauthenticated sessions simultaneously

## Slide 5: Example Provisioning Model
+------------+
| Controller |
+------------+
/ \
Destination UDP Port / \ Destination UDP port
Authentication Mode & Key / \ Authentication Mode & Key
Delay Measurement Mode / \ Synthetic/Connection Loss
Timestamp Format / \ Direct Measurement Mode
Synthetic/Connection Loss / \
Direct Measurement Mode / \
v v
+-------+ +-------+
| | | |
| R1 |============| R3 |
| | SR path | |
+-------+ Or link +-------+
Session-Sender Session-Reflector

## Slide 6: Session-Sender Test Packet for Links
User-configured destination UDP port1 is used for STAMP test packets, using local and remote link addresses
User-configured destination UDP port2 is used for direct measurement test packets for packet loss
Applicable to physical, virtual, LAG, LAG member, numbered/unnumbered links
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.2 of RFC 8762 or |
. Payload = Direct Measurement Test Packet .
. .
+---------------------------------------------------------------+
Figure 1: Session-Sender Test Packet for links

## Slide 7: Session-Sender Test Packet for SR-MPLS and SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Test packet including IP/UDP Header from Figure 1 |
. .
+---------------------------------------------------------------+
Figure 2: Example session-sender test packet for SR-MPLS Policy
For performance delay/loss measurement of end-to-end SR Policy, the test packet is sent on the SR Policy with:
MPLS label stack of SR-MPLS Policy
SRv6 SRH [RFC 8754] with Segment List of SRv6 Policy
User-configured destination UDP port1 is used for STAMP test packets
User-configured destination UDP port2 is used for direct measurement test packets for packet loss
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Session-Reflector IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.2 of RFC 8762 or |
. Payload = Direct Measurement Test Packet .
. .
+---------------------------------------------------------------+
Figure 3: Example session-sender test packet for SRv6 Policy

## Slide 8: Session-Reflector Test Packet
The test packet reply is sent using the IP/UDP information from the received test packet.
Use Control Code from the received test packet if set.
Use Segment List from Return Path TLV if present in received test packet.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Reflector IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from test packet .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Reflector .
. Destination Port = Source Port from test packet .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.3 of RFC 8762 or |
. Payload = Direct Measurement Reply test packet .
. .
+---------------------------------------------------------------+
Figure: Session-Reflector Test Packet

## Slide 9: ECMP Support for SR Path
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending test packets that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to test packets. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8)
    Identify intended actual destination node in “Destination Node Address TLV”
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 10: Performance Measurement Modes
One-way Measurement Mode
  Test packet reply sent “out of band” on IP/UDP path by default
Two-way Measurement Mode
  Test packet reply sent “in-band” on reverse path
    Use Control Code from the received test packet
    Use Return Path TLV for STAMP from the received test packet
Loopback Measurement Mode
  Test packet carries the return path in the header

## Slide 11: Example PM Metrics
Compute following delay metrics:
  Minimum delay
  Maximum delay
  Average delay
  Delay variance
Compute following loss metrics:
  Synthetic packet loss (aka indirect-mode packet loss)
  Connection loss (aka liveness heart-beat failure detection)

## Slide 12: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 13
Thank you