## Slide 1: Performance Measurement in Segment Routing Networks with MPLS Data Plane
draft-gandhi-spring-sr-mpls-pm-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Sagar Soni - Cisco Systems (sagsoni@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)
Pier Luigi Ventre - CNIT (pierluigi.ventre@cnit.it)
Mach Chen - Huawei (mach.chen@huawei.com)
Patrick Khordoc - Cisco Systems (pkhordoc@cisco.com)
Zafar Ali - Cisco Systems (zali@cisco.com)
Daniel Bernier - Bell Canada (daniel.bernier@bell.ca)

## Slide 2: Agenda
Requirements and Scope
In-band Probes for SR Links and SR Policies
DM and LM Packets for SR Links and SR Policies
Probe Responses
SR Link Extended TE Metrics Advertisements
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and loss Performance Measurement (PM) for SR links and end-to-end SR Policies
  Delay and loss extended TE link metrics advertisement in the network
  Scope:
    Segment Routing (SR) with MPLS data plane
    In-band PM probe messages
    Use RFC 6374 (defined for MPLS-TP) based mechanisms
    Use RFC 7876 (UDP return path) for probe response messages
    Informational

## Slide 4: PM Probes for SR Links
For SR links, the PM probe query messages for link delay and packet loss measurements are sent in-band using MPLS GAL/GAch header as defined in [RFC6374].

## Slide 5: PM Probes for SR Policies
For end-to-end measurement of SR Policies, the PM probe query messages for delay and loss measurements are sent in-band using MPLS GAL/GAch header as defined in [RFC6374] and SR-MPLS label stack.

## Slide 6: DM Probes for SR Links and SR Policies
DM probes use the message format defined in [RFC6374] as payload.
  GAL : 13
  GAch : 0x000C

## Slide 7: LM Probes for SR Links and SR Policies
LM probes use the message format defined in [RFC6374] as payload.
  GAL : 13
  GAch : 0x000A (Direct)
  0x000B (Inferred)

## Slide 8: Probe Responses
One-way Measurement Response (out-of-band)
  Sent to the querier node using the information from the UDP Return Object (URO) TLV [RFC7876].
  URO TLV is sent by the querier node in the probe query messages and contains the UDP destination port and IP address.
Two-way Measurement Response (in-band)
  Sent to the querier node using a message similar to the in-band probe query message as SR-MPLS packet.

## Slide 9: SR Link Extended TE Metrics Advertisement
PM procedure is used to measure delay and loss performance of SR Links.
Compute SR Link Delay metrics (minimum-delay, maximum-delay, average-delay, delay-variance) and SR Link Packet Loss metric.
SR link extended TE metrics advertised in the network using the TLVs defined in the following RFCs/Drafts:
  OSPF [RFC7471]
  ISIS [RFC7810] [draft-ietf-lsr-isis-rfc7810bis]
  BGP-LS [draft-ietf-idr-te-pm-bgp]

## Slide 10: Next Steps
Welcome your comments and suggestions
Multiple implementations already exist
Request for WG adoption

## Slide 11
Thank you.