## Slide 1: Enhanced Performance Measurement and Liveness Monitoring in Segment Routing Networks
draft-gandhi-spring-sr-enhanced-plm-01
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Navin Vaghamshi - Reliance (Navin.Vaghamshi@ril.com)
Moses Nagarajah - Telstra (Moses.Nagarajah@team.telstra.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Performance Delay Measurement & Liveness Monitoring in SR networks
    End-to-end P2P/P2MP SR paths
    Applicable to SR-MPLS/SRv6 data planes
    Support ECMP SR paths
  Running single protocol for liveness detection and performance measurement in SR networks
    Simplify deployment and reduce operational complexity
  No endpoint dependency
    Stateless on endpoint (e.g. endpoint unaware of the probe protocol)
    Higher scale and faster detection interval (e.g. packets not punted out of fast-path)
  Scope:
  RFC 5357 (TWAMP Light) defined probe messages
  RFC 8762 (STAMP) defined probe messages
  User-configured IP/UDP path for probe messages

## Slide 4: History of the Draft
March 2020
  Draft was published
April 2020
  Presented version 00 in IETF MPLS WG Virtual Meeting

## Slide 5: Liveness and Performance Monitoring of SR Policy
Liveness monitoring for SR Policy uses PM probes (TWAMP Light/STAMP delay measurement messages) in Loopback Mode
Probe messages sent using Segment List(s) of the SR Policy Candidate Path(s)
Probe messages are not punted on the remote node (endpoint/reflector) out of fast-path
Return path can be IP or SR
Liveness failure is notified when consecutive N number of probe messages are not received back at the sender
Round-trip delay metrics are notified when consecutive M number of probe messages have delay values exceed the configured thresholds
+-------+ t1 Probe +-------+
| | - - - - - - - - - - | |
| R1 |====================|| R5 |
| |<- - - - - - - - - - | |
+-------+ t4 Return Probe +-------+
Sender Reflector Endpoint
(Simply Forward)
Figure: Loopback Mode

## Slide 6: Enhanced Liveness and Performance Monitoring of SR Policy
Use PM probes in loopback mode enabled with network programming function
  The network programming function optimizes the "operations of punt, add receive timestamp and inject the probe packet" on the reflector node
The endpoint node adds the receive timestamp in the payload of the received TWAMP Light or STAMP probe message without punting the probe message
  Only add the receive timestamp if the source address in the probe message matches the local node address
Liveness failure is notified when consecutive N number of probe messages are not received back at the sender
One-way delay metrics are notified when consecutive M number of probe messages have delay values exceed the configured thresholds
+-------+ t1 Probe t2 +-------+
| | - - - - - - - - - - | |
| R1 |====================|| R5 |
| |<- - - - - - - - - - | |
+-------+ Return Probe +-------+
Sender Reflector Endpoint
(Timestamp,
Pop and Forward)
Figure: Loopback Mode Enabled with Network Programming

## Slide 7: Probe Message – Enhanced Loopback Mode
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | |
+-+-+-+-+-+-+-+-+ |
| |
~ Padding ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: TWAMP Light Probe Message Format
Sender adds the Transmit Timestamp
Reflector adds the Receive Timestamp at fixed offset locally provisioned (consistently in the network)
  E.g. offset-byte 16 from the start of the payload
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: STAMP Probe Message Format

## Slide 8: SR-MPLS with Timestamp and Forward Function
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Label(1) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ . . . . . . +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Label(n) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Timestamp Label (TBA1) | TC |S| TTL | +---------------------------------------------------------------+ | IP Header | . Source IP Address = Endpoint IPv4 or IPv6 Address . . Destination IP Address = Sender IPv4 or IPv6 Address . . Protocol = UDP . . . +---------------------------------------------------------------+ | UDP Header | . Source Port = As chosen by Sender . . Destination Port = User-configured Port . . . +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Payload as defined in Section 4.2.1 of RFC 5357 | | Payload as defined in Section 4.2 of RFC 8762 | . . +---------------------------------------------------------------+ Figure 6: Example Probe Message for SR-MPLS with Timestamp Label
Extended Special-purpose label (TBA1) is defined for Timestamp and Forward network function
Reverse Path can be IP or SR-MPLS
Source and Destination Addresses are swapped to represent the Reverse direction path

## Slide 9: ECMP Support for SR Paths
SR Paths can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8) when return path is SR-MPLS
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 10: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Network Programming Label
Measurement Protocol / \ Timestamp2 Offset
PLM Type / \ Timestamp Format
LB or Enhanced LB / \
Authentication Mode & Key / \
Network Programming Label / \
Timestamp Format / \
/ \
v v
+-------+ +-------+
| | SR Path | |
| R1 |============| R5 |
| | | |
+-------+ +-------+
Sender Reflector

## Slide 11: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 12
Thank you

## Slide 13
Backup

## Slide 14: SRv6 with Timestamp and Forward Function Example 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv6 Address .
. Destination IP Address = Next IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. END.TSF with Target SID .
. .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Reflector IPv6 Address .
. Destination IP Address = Sender IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload as defined in Section 4.2.1 of RFC 5357 | |
| Payload as defined in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Example 1: Probe Message for SRv6 with Endpoint Function IP Return Path
Endpoint Function END.TSF is defined for Timestamp and Forward and carried for the Reflector node SID
Reverse Path is IP
Reflector node removes SRH
Inner IPv6 header is required
  Source and Destination Addresses are swapped to represent the Reverse direction path in the inner IPv6 header

## Slide 15: SRv6 with Timestamp and Forward Function Example 2
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv6 Address .
. Destination IP Address = Next IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. END.TSF with Target SID .
. .
+---------------------------------------------------------------+
| IP Header (Optional) |
. Source IP Address = Reflector IPv6 Address .
. Destination IP Address = Sender IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload as defined in Section 4.2.1 of RFC 5357 | |
| Payload as defined in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Example 2: Probe Message for SRv6 with Endpoint Function SR Return Path
Endpoint Function END.TSF is defined for Timestamp and Forward and carried for the Reflector node SID
Reverse direction SR path carried in SRH
Reflector node does not remove the SRH
Inner IPv6 header is optional and not required
  Source and Destination Addresses are swapped to represent the Reverse direction path in the inner IPv6 header

## Slide 16
Thank you