## Slide 1: UDP Path for In-band Performance Measurement for Segment Routing Networks
draft-gandhi-spring-udp-pm-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)
Pier Luigi Ventre - CNIT (pierluigi.ventre@cnit.it)
Mach Chen - Huawei (mach.chen@huawei.com)
Sagar Soni - Cisco Systems (sagsoni@cisco.com)
Patrick Khordoc - Cisco Systems (pkhordoc@cisco.com)
Zafar Ali - Cisco Systems (zali@cisco.com)
Daniel Bernier - Bell Canada (daniel.bernier@bell.ca)
Dirk Steinberg - Steinberg Consulting (dws@dirksteinberg.de)

## Slide 2: Agenda
Requirements and Scope
Probe Query Message
Probe Response Message
Return Path, Sequence Number and Block Number TLVs
ECMP Support
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM) for SR links and end-to-end P2P and P2MP SR Policies
  Applicable to SR-MPLS/SRv6 data planes
  No need to bootstrap PM session (e.g., to negotiate UDP port) - spirit of SR
  Stateless on egress node - spirit of SR
  One-way and two-way measurements
  Handle ECMP for SR Policies
  Scope:
  Use RFC 6374 defined probe message formats
  Use RFC 7876 (IP/UDP return path) defined probe response messages
  Define IP/UDP path for PM probe query messages

## Slide 4: Probe Query Messages
IP/UDP path is defined for PM probe query messages for delay and loss measurements for SR links and end-to-end P2P and P2MP SR Policies.
For end-to-end performance measurement, the probe query messages are sent in-band with MPLS label stack SR-MPLS Policies and SRv6 SRH with SID list for SRv6 Policies.
Payload contains [RFC6374] defined message for DM or LM.
UDP port IANA-TBA1 is used for identifying DM probe packets.
UDP port IANA-TBD2 is used for identifying LM probe packets.

## Slide 5: Probe Response Messages
Probe response messages can be sent in-band (two-way measurement) or out-of-band (one-way measurement) for SR links and SR Policies.
Use the information from the UDP Return Object (URO) TLV [RFC7876] from the received Probe query message payload, otherwise use the IP/UDP information (Source IP Address and Source UDP port) from the received Probe query message header.

## Slide 6: Return Path TLV
For two-way end-to-end performance measurement of SR Policies, the responder node needs to send the probe response messages in-band on a specific reverse SR path.
Querier node can request the responder node to send the probe response messages back on a given reverse path (e.g. co-routed path) by adding a Return Path Segment List (RPSL) TLV in the probe query messages.
TBA3: SR-MPLS RPSL
TBA4: SRv6 RPSL
TBA5: SR-MPLS BSID
TBA6: SRv6 BSID

## Slide 7: Sequence Number TLV
Define Sequence Number TLV for Probe Query and Response messages.
Useful when some probe query messages are lost or they arrive out of order.

## Slide 8: Block Number TLV
Define Block Number TLV for Probe Query and Response messages.
[RFC8321] requires to identify the Block Number (color) of the traffic counters carried by the probe query and response messages.

## Slide 9: ECMP Support
SR Policy can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages:
  For IPv4 and IPv6
    Different Destination/Source Addresses or Source UDP ports in IP/UDP header.
  For SR-MPLS
    Entropy label.
  For SRv6
    Flow Label in SRH.

## Slide 10: Next Steps
Welcome your comments and suggestions
Implementations of building blocks already exist (e.g. RFC6374, IP/UDP paths for probes as in RFC7876)
Request for WG adoption

## Slide 11
Thank you.