## Slide 1: PCEP Extensions for Associated Bidirectional Label Switched Paths (LSPs) with Stateful PCE
draft-ietf-pce-association-bidir-06
Rakesh Gandhi (rgandhi@cisco.com)
Colby Barth (cbarth@juniper.net)
Bin Wen (Bin_Wen@comcast.com)

## Slide 2: Agenda
Requirements and Scope
Double-sided Associated Bidirectional LSP
Single-sided Associated Bidirectional LSP
PCEP Object Definitions
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Packet transport networks deploying bidirectional RSVP LSPs
  Co-routed and non-co-routed forward and reverse RSVP LSPs
Scope:
  Associated bidirectional RSVP LSPs
  PCE-Initiated LSPs
  PCC-Initiated LSPs
  Stateless PCE (e.g. for co-routed path computation requests)

## Slide 4: Single-sided Associated Bidirectional LSP
Tunnel-AD
STATEFUL PCE
PCC End-point-A
End-point-D
Node-B
Node-C
LSP1 (F,C)
LSP2 (R,C)
PCE or PCC Initiated LSPs
Association initiated by PCC or PCE
Co-routed or non-co-routed
Endpoint-A signals RSVP REVERSE_LSP Object in LSP1 Path message for reverse LSP2

## Slide 5: Double-sided Associated Bidirectional LSP
Tunnel-DA
Tunnel-AD
STATEFUL PCE
PCC End-point-A
PCC End-point-D
Node-B
Node-C
LSP1 (F,C)
LSP2 (F,C)
PCE or PCC Initiated LSPs
Association initiated by PCE or PCC
Co-routed or non-co-routed
B flag in RP object

## Slide 6: PCEP Association Object
Association Type (TBD1) = Single-sided Bidirectional LSP Association Group
Association Type (TBD2) = Double-sided Bidirectional LSP Association Group
The Association ID, Association Source, Global Association Source and Extended Association ID in the Association Object of the bidirectional LSPs are populated using the procedures defined in [RFC7551].
These Association Types are operator-configured associations.
  Operator-configured Association Range TLV (Type 29) SHOULD NOT be sent, so that the entire range of association ID can be used.

## Slide 7: Bidirectional LSP Association Group TLV
F (Forward LSP, 1 bit)
  Indicates whether the LSP associated is the forward LSP of the bidirectional LSP.
R (Reverse LSP, 1 bit)
  Indicates whether the LSP associated is the reverse LSP of the bidirectional LSP.
C (Co-routed LSP, 1 bit)
  Indicates whether the associated bidirectional LSP is co-routed.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = TBD3 | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved |C|R|F|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Bidirectional LSP Association Group TLV format

## Slide 8: Error Handling (PCErr Error-Type 26 - Association Error)
Both forward and reverse LSPs MUST belong to the same bidirectional TE tunnel [RFC3209].
  Error-Value = Bidirectional LSP Association - Tunnel mismatch
LSP (forward or reverse) cannot be part of more than one Bidirectional LSP Association Group.
  Error-Value = Bidirectional LSP Association - Group Mismatch
If a PCEP speaker receives a different PST value for Bidirectional LSP association group and it does not support.
  Error-Value = Bidirectional LSP Association - Path Setup Type Not Supported

## Slide 9: Next Steps
Welcome your review comments and suggestions
In the WG LC Queue

## Slide 10
Thank you