## Slide 1: PCEP Extensions for Associated Bidirectional SR Paths
draft-ietf-pce-sr-bidir-path-02
Cheng Li (chengli13@huawei.com)
Mach(Guoyi) Chen (Mach.chen@huawei.com)
Weiqiang Cheng (chengweiqiang@chinamobile.com)
Rakesh Gandhi (rgandhi@cisco.com) - Presenter
Quan Xiong (xiong.quan@zte.com.cn)

## Slide 2: Agenda
Requirements and Scope
Double-sided Associated Bidirectional with Reverse LSP
PCEP Object Definitions
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Packet transport networks deploying bidirectional SR Paths
  Co-routed and non-co-routed forward and reverse SR Paths
Scope:
  Associated bidirectional SR Paths
  PCE-Initiated LSPs
  PCC-Initiated LSPs
  Stateless PCE (e.g. for co-routed path computation requests)
Not in Scope:
  Associating a bidirectional SR Path with an RSVP LSP

## Slide 4: Double-sided Associated Bidirectional with Reverse LSP
STATEFUL PCE
PCC End-point-A
PCC End-point-D
Node-B
Node-C
PCE Initiated LSPs
Association initiated by PCE or PCC
Co-routed or non-co-routed
B flag in RP object
Tunnel-AD
LSP1 (F,C)
LSP2 (R,C)
Tunnel-DA
LSP1 (R,C)
LSP2 (F,C)
PCInitiate
PCInitiate

## Slide 5: Double-sided Associated Bidirectional with Reverse LSP
STATEFUL PCE
PCC End-point-A
PCC End-point-D
Node-B
Node-C
PCC Initiated LSPs
Association initiated by PCE or PCC
Co-routed or non-co-routed
B flag in RP object
Tunnel-AD
LSP1 (F,C)
LSP2 (R,C)
Tunnel-DA
LSP1 (R,C)
LSP2 (F,C)
PCReport/
PCUpdate
PCReport/
PCUpdate

## Slide 6: PCEP Association Object
Association Type (TBD1) = Double-sided Bidirectional with Reverse LSP Association Group
The Association Object Populated using the procedure defined in [draft-ietf-pce-association-bidir]

## Slide 7: Error Handling (PCErr Error-Type 26 - Association Error)
PCErr defined in [draft-ietf-pce-association-bidir] are applicable to SR Paths
Specifically –
Both forward and reverse LSPs MUST belong to the same bidirectional TE tunnel [RFC3209].
  Error-Value = Bidirectional LSP Association - Tunnel mismatch
LSP (forward or reverse) cannot be part of more than one Bidirectional LSP Association Group.
  Error-Value = Bidirectional LSP Association - Group Mismatch
If a PCEP speaker receives a different PST value for Bidirectional LSP association group and it does not support.
  Error-Value = Bidirectional LSP Association - Path Setup Type Not Supported

## Slide 8: Next Steps
Welcome your review comments and suggestions

## Slide 9
Thank you