## Slide 1: Enhanced Performance and Liveness Monitoring in Segment Routing Networks
draft-gandhi-spring-sr-enhanced-plm-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Navin Vaghamshi - Reliance (Navin.Vaghamshi@ril.com)
Moses Nagarajah - Telstra (Moses.Nagarajah@team.telstra.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Performance Delay and Loss Monitoring & Liveness Monitoring
    End-to-end P2P/P2MP SR Policies
    Applicable to SR-MPLS/SRv6 data planes
  Scope:
  RFC 5357 (TWAMP) defined probe messages - TWAMP Light
  STAMP [draft-ietf-ippm-stamp] defined probe messages
  STAMP TLVs [draft-ietf-ippm-stamp-option-tlv]
  User-configured IP/UDP path for probe messages

## Slide 4: Liveness Monitoring Using PM
Liveness monitoring for SR Policy uses Loopback Mode for PM probes (TWAMP Light/STAMP delay measurement messages)
Probe messages sent using Segment List(s) of the SR Policy Candidate Paths
Probe messages are not punted to the remote/end-point/reflector node
Liveness failure is notified when consecutive N number of probe messages are not received back at the sender, where N is locally provisioned value.
+-------+ t1 Probe +-------+
| | - - - - - - - - - - | |
| R1 |--------------------|| R5 |
| |<- - - - - - - - - - | |
+-------+ t4 Return Probe +-------+
Sender Reflector Endpoint
(Simply Forward)
Figure 1: Loopback Mode

## Slide 5: Probe Query Message in Loopback Mode
User-configured destination UDP port1 is used for DM probe messages in unauthenticated mode.
The payload contains RFC 5357 (TWAMP Light) or STAMP defined probe message.
Source and Destination IP Addresses set for the reverse direction path
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Reflector IPv4 or IPv6 Address .
. Destination IP Address = Sender IPv4 or IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port for Delay Measurement.
. .
+---------------------------------------------------------------+
| Payload = Message as specified in Section 4.2.1 of RFC 5357 |
. Payload = Message specified in Section 4.2 of ietf-ippm-stamp .
. .
+---------------------------------------------------------------+
Figure: DM Probe Query Message

## Slide 6: Enhanced Liveness Monitoring Using PM
Use the loopback mode enabled with network programming function.
The network programming function optimizes the "operations of punt, add receive timestamp and inject the probe packet" on the reflector node.
The endpoint node adds the receive timestamp (at the fixed location locally provisioned consistently in the network) in the payload of the received TWAMP Light or STAMP probe message without punting the probe message in control-plane.
Only add the receive timestamp if the source address in the probe message matches the local node address
+-------+ t1 Probe t2 +-------+
| | - - - - - - - - - - | |
| R1 |--------------------|| R5 |
| |<- - - - - - - - - - | |
+-------+ Return Probe +-------+
Sender Reflector Endpoint
(Timestamp,
Pop and Forward)
Figure: Loopback Mode Enabled with Network Programming

## Slide 7: Next Steps
Welcome your comments and suggestions
Implementation exists
Requesting WG adoption

## Slide 8
Thank you

## Slide 9: Backup

## Slide 10: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Destination UDP port
Measurement Protocol / \ Measurement Protocol
Measurement Type / \ Measurement Type
Delay/Loss / \ Delay/Loss
Authentication Mode & Key / \ Authentication Mode & Key
Timestamp Format / \ Loss Measurement Mode
Delay Measurement Mode / \
Padding/Packet Size / \
Loss Measurement Mode / \
v v
+-------+ +-------+
| | | |
| R1 |------------| R5 |
| | | |
+-------+ +-------+
Sender Reflector

## Slide 11: Probe Query for SR-MPLS and SRv6 Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message for DM |
. .
+---------------------------------------------------------------+
Figure: Probe Query Message for SR-MPLS Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| SRH |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message for DM |
. (Using IPv6 Addresses) .
. .
+---------------------------------------------------------------+
Figure: Probe Query Message for SRv6 Policy
For end-to-end performance delay/loss measurement of SR Policy, the probe query messages are sent on the SR Policy path with:
MPLS label stack for SR-MPLS Policies,
SRv6 SRH [draft-ietf-6man-segment-routing-header] with SID list for SRv6 Policies.

## Slide 12: ECMP Support for SR Policy
SR Policy can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages:
  For IPv4 and IPv6
    Destination addresses in IP header (e.g. 127/8 for IPv4 and FFFF:7F00/104 for IPv6)
    Flow label in IPv6 header

## Slide 13
Thank you