## Slide 1: Performance Measurement Using Simple TWAMP for Segment Routing Networks
draft-gandhi-spring-stamp-srpm-04
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
Summary of Procedures
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Synthetic Loss Performance Measurement (PM)
    Links and End-to-end P2P/P2MP SR Paths
      Links include physical, virtual, LAG (bundle), LAG member, numbered/unnumbered links
    Applicable to SR-MPLS/SRv6 data planes
  No need to signal to PM parameters - spirit of SR
    Stateless on egress node - spirit of SR
    State is in the probe message
  Handle ECMP for SR Paths
  Support stand-alone direct-mode loss measurement
  Scope:
  STAMP [RFC 8762]
  STAMP TLVs [draft-ietf-ippm-stamp-option-tlv]

## Slide 4: Review Comments
Add references for well-known terms “Link”, “SR Path”, and “Congruent paths”
Destination UDP port used has zero UDP checksum for IPv6 header
  Add Reference for RFC 6936 in Security Section
  For IPv4 and IPv6 probe messages, where the hardware is not capable of re-computing the UDP checksum or adding checksum complement [RFC7820], the sender node MAY set the UDP checksum to 0 [RFC8085] and reflector node MAY accept it as long as it meets requirements specified in [RFC6936]
Add reference for Yang data model draft in provisioning model section
Liveness is to compute “connection loss” performance metric
  Similar to the widely deployed synthetic packet loss metric
Editorial
  Indicate packet loss is direct-mode loss
  Use test packet term for query message
  H/W timestamps required -> H/W timestamps recommended
  IPv6 address ::1/128 or ::FFFF:127/104
  Clarify - Section 4.1.4.2 and 4.2.2.2 depict the packet format with word “as needed” for inner IP Header
  Different UDP destination ports when running authenticated and unauthenticated sessions simultaneously

## Slide 5: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Destination UDP port
Measurement Protocol / \ Measurement Protocol
Measurement Type / \ Measurement Type
Delay/Loss / \ Delay/Loss
Authentication Mode & Key / \ Authentication Mode & Key
Timestamp Format / \ Loss Measurement Mode
Delay Measurement Mode / \ SSID - Wildcard
Loss Measurement Mode / \
v v
+-------+ +-------+
| | | |
| R1 |============| R5 |
| | SR Path | |
+-------+ Or Link +-------+
Session-Sender Session-Reflector

## Slide 6: Probe Query for Links
User-configured destination UDP port1 is used for DM probe messages and port2 is used for direct-mode LM probe messages (unauthenticated mode)
Applicable to physical, virtual, LAG, LAG member, numbered/unnumbered links – probe messages pre-routed over the links
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = DM Message specified in Section 4.2 of RFC 8762 or |
. Payload = LM Message specified in this document .
. .
+---------------------------------------------------------------+
Figure: Probe Query Message

## Slide 7: Probe Query for SR-MPLS and SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DM or LM Query Message including IP/UDP Header |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SR-MPLS Policy
For performance delay/loss measurement of end-to-end SR Policy, the probe query message is sent on the SR Policy with:
MPLS label stack of SR-MPLS Policy
SRv6 SRH [RFC 8754] with Segment List of SRv6 Policy
User-configured destination UDP port1 is used for DM probe messages and port2 is used for direct-mode LM probe messages (unauthenticated mode) – same as Links.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. .
+---------------------------------------------------------------+
| IP Header (as needed) |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Session-Reflector IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = DM or LM Query Message |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SRv6 Policy

## Slide 8: Probe Response Message
The probe response message is sent using the IP/UDP information from the probe query message.
Based on Control Code from the probe query message
Use Segment List from Return Path TLV if present in probe query message.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Reflector IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from Query .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Reflector .
. Destination Port = Source Port from Query .
. .
+---------------------------------------------------------------+
| Payload = DM Response Message | |
. Payload = LM Response Message .
. .
+---------------------------------------------------------------+
Figure: Probe Response Message

## Slide 9: ECMP Support for SR Path
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to probe messages. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8)
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 10: Performance Measurement Modes
One-way Measurement Mode
  Reply sent “out of band” on IP/UDP path by default
Two-way Measurement Mode
  Reply sent “in-band” on reverse SR path
    Based on Control Code from the probe query message
  Use Return Path TLV for STAMP from the probe query message
Loopback Measurement Mode
  Probe message carries the return path in the header of the packet

## Slide 11: Example PM Metrics
PM probe packets can be used to compute following delay metrics:
  Minimum delay
  Maximum delay
  Average delay
  Delay variance
PM probe packet loss can be used to compute following loss metrics:
  Synthetic packet loss (aka indirect-mode packet loss measurement)
  Connection loss (aka liveness heart-beat failure detection)

## Slide 12: Next Steps
Welcome your comments and suggestions

## Slide 13
Thank you