## Slide 1: MPLS Data Plane Encapsulation for In-situ OAM Data
draft-gandhi-mpls-ioam-sr-05
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Zafar Ali - Cisco Systems (zali@cisco.com)
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Frank Brockners - Cisco Systems (fbrockne@cisco.com)
Bin Wen - Comcast (Bin_Wen@cable.comcast.com)
Voitek Kozak - Comcast (Voitek_Kozak@comcast.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Transport In-situ OAM (IOAM) data fields with MPLS Encapsulation
  Scope:
  Using data fields defined in:
    draft-ietf-ippm-ioam-data
    draft-ietf-ippm-ioam-direct-export
    draft-ietf-ippm-ioam-flags
  Edge-to-edge (E2E) IOAM
  Hop-by-hop (HbH) IOAM

## Slide 4
IOAM Header

## Slide 5: IOAM Data Field Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM Encapsulation in MPLS Header

## Slide 6: IOAM G-ACh Header
New Generic Associated Channel (G-ACh) Type (value TBA3) defined for IOAM
Protocol value 0001b allows to avoid incorrect IP header based hashing over ECMP paths
Block Number can be used to:
  Aggregate IOAM data collected in data plane, e.g. compute measurement metrics for each block of a flow
  Correlate IOAM data from different nodes

## Slide 7: IOAM Indicator Label
“IOAM Indicator Label” is used to indicate the presence of the IOAM data fields after EOS in the MPLS header. How to process the IOAM data field(s) depends on the IOAM Option-Type.
Separate Indicator Labels are used for E2E IOAM (for edge nodes) and HbH IOAM (for edge and transit nodes) to optimize the IOAM processing on transit nodes when not needed.
In case of E2E IOAM, the IOAM Option-Type(s) in the data packets are processed on edge nodes only. The transit nodes ignore the IOAM Option-Type(s) carried by the data packets.
In case of HbH IOAM, the IOAM Option-Type(s) in the data packets are processed on transit and edge nodes.

## Slide 8
E2E IOAM

## Slide 9: E2E IOAM Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| E2E IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: E2E IOAM Encapsulation in MPLS Header

## Slide 10: E2E Indicator Label Allocation Methods
Extension Label (15) and Label assigned by IANA with value TBA1
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating and decapsulating nodes
The IOAM Enabled Label allocated by the decapsulating node
  Signaling/advertisement extensions needed to convey the label to all encapsulating nodes (out of scope)

## Slide 11: E2E Indicator Label Allocation Methods
 | Method | Extra Label Stack Size (Note 2) | Location on Stack
1 | eSPL Labels | +2 (Note 1) | Bottom
2 | Global Label | +1 | Bottom
3 | Signal/Advertise Label | +1 (compared to PHP) | Bottom
This is true for any mechanism that we are defining using eSPL
  SFC: https://tools.ietf.org/html/rfc8595
  E2E: draft-cheng-mpls-inband-pm-encapsulation
IOAM data packets may require Entropy label for ECMP

## Slide 12: E2E IOAM Procedure
The encapsulating node inserts an E2E Indicator Label and one or more IOAM data field(s) in the MPLS header.
The transit (intermediate) nodes do not process IOAM data.
The decapsulating node "punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node for E2E IOAM also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.
  The decapsulating node processes IOAM data field(s).
  The decapsulating node forwards the data packet downstream.

## Slide 13
HbH IOAM

## Slide 14: HbH IOAM Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| HbH IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: HbH IOAM Encapsulation in MPLS Header

## Slide 15: HbH Indicator Label Allocation Methods
Extension Label (15) and Label assigned by IANA with value TBA2
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating, transit and decapsulating nodes
The IOAM Enabled Label allocated by the transit and decapsulating nodes
  Signaling/advertisement extensions needed to convey the label to all encapsulating nodes (out of scope)

## Slide 16: HbH Indicator Label Allocation Methods
 | Method | Extra Label Stack Size (Note 4) | Location on Stack | Scan Label Stack (Notes 3) | Different FIB Entry for Local Label
1 | eSPL Labels | +2 | Bottom (Note 1) | Yes (Note 2) | No
2 | Global Label | +1 | Bottom | Yes (Note 2) | No
3 | Signal/Advertise Label (like SFL) | +0 | Incoming Packet with Top Label | No | Yes
eSPL at top of the label stack breaks MPLS forwarding in heterogenous network environment with and without IOAM capable nodes
Entropy Label similarly also requires transit nodes to scan label stack, however, entropy label processing is optional whereas IOAM processing is not optional.
A transit node may have a limit on how many labels it can scan. With any indicator scheme, the node will have to look past EOS into the packet to find the IOAM data that needs to be processed
IOAM data packets may require Entropy label for ECMP

## Slide 17: HbH IOAM Procedure
The encapsulating node inserts a HbH Indicator Label and one or more IOAM data field(s) in the MPLS header.
The transit (intermediate) node processes HbH IOAM data field(s) and forwards the data packet including updated IOAM data field(s).
  Transit node (intermediate) may punt the timestamped copy of the data packet for further IOAM processing
The decapsulating node "punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node for E2E IOAM also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.
  The decapsulating node processes IOAM data field(s).
  The decapsulating node forwards the data packet downstream.

## Slide 18: HbH IOAM Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| HbH IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: HbH IOAM Encapsulation in MPLS Header

## Slide 19: HbH IOAM Encapsulation Example with SR-MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PSID | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| HbH IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM Encapsulation Example with SR-MPLS Header

## Slide 20: Next Steps
Welcome your comments and suggestions
Requesting MPLS WG adoption

## Slide 21
Thank you

## Slide 22
Open Review Comments

## Slide 23: IOAM Data After EOS
What if the LSP is carrying a PW or is DetNet?
What if it is a MS-PW?
In all these cases there is a CW immediately after EOS
Then there is the universal fragmentation idea that is floating about that also wants to follow EOS
Reply:
IOAM data is part of the MPLS Header and PW/DetNet header/data is carried below the IOAM header.
The decap node removes the MPLS header including the IOAM header and then processes the PW/DetNet header/data.

## Slide 24: IOAM Encapsulation in MPLS Header with PW Data
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| HbH IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | PW G-ACh |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: HbH IOAM Encapsulation in MPLS Header

## Slide 25
Thank you