## Slide 1: Performance Measurement Using Simple TWAMP for Segment Routing Networks
draft-gandhi-spring-stamp-srpm-05
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
Summary of Procedure
Next Steps

## Slide 3: Requirements, Goals and Scope
Requirements:
  In-band Performance Delay and Loss Measurement
    Links and end-to-end P2P/P2MP SR paths
      Links include physical, virtual, LAG, LAG member links
    Applicable to SR-MPLS/SRv6 data planes
  One-way, two-way, round-trip delay and packet loss metrics
Goals:
  Avoid provisioning and maintaining each test session on Session-Reflector
  Avoid control protocol for signaling dynamic parameters
  Scope:
  STAMP [RFC 8762]
  STAMP Extensions [RFC 8972]
  STAMP Extensions for SR [draft-gandhi-ippm-stamp-srpm]

## Slide 4: Updates Since Version-02
Updates:
  Draft status - Informational
  Updated terminology to align with STAMP
  Added (synthetic) packet loss section
  Removed stand-alone direct measurement messages
  Removed text for IPv6/UDP test packet with zero checksum
  Various editorial changes to address review comments
  Open Items:
    None

## Slide 5: Example STAMP Reference Model
+------------+
| Controller |
+------------+
/ \
Destination UDP Port / \ Destination UDP port
Authentication Mode & Key / \ Authentication Mode & Key
Delay Measurement Mode / \
Timestamp Format / \
Packet Loss Type / \
/ \
v v
+-------+ +-------+
| | | |
| R1 |============| R3 |
| | | |
+-------+ +-------+
STAMP Session-Sender STAMP Session-Reflector

## Slide 6: STAMP Session-Sender Test Packet for Links
For links, STAMP Session-Sender test packets are transmitted over the links using local and remote link addresses
User-configured destination UDP port is used for STAMP test packets (or port 862)
IPv4 TTL /IPv6 Hop-limit is set to 1
Applicable to physical, virtual, LAG, LAG member links
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port | 862 .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure 1: STAMP Session-Sender Test Packet for links

## Slide 7: STAMP Session-Sender Test Packet for SR-MPLS and SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Test Packet including IP/UDP Header from Figure 1 |
. .
+---------------------------------------------------------------+
Figure 2: Example Session-Sender test packet for SR-MPLS Policy
For end-to-end SR Policy, STAMP Session-Sender test packets are transmitted with:
  MPLS label stack of SR-MPLS Policy
  SRv6 SRH [RFC 8754] with Segment List of SRv6 Policy
    Using upper-layer processing defined in SRv6 network programming
User-configured destination UDP port is used for STAMP test packets (or port 862)
IPv4 TTL/IPv6 Hop-limit is set to 255
Color-Only Destination Steering:
  IPv4
    Destination Address in 127/8 range
    TTL is set to 1
  IPv6
    Destination Address set to ::1/128
    Hop Limit is set to 1
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Session-Reflector IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port | 862 .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure 3: Example Session-Sender test packet for SRv6 Policy

## Slide 8: STAMP Session-Sender Test Packet for P2MP SR-MPLS Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Tree-SID | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Test Packet including IP/UDP Header from Figure 1 |
. .
+---------------------------------------------------------------+
Figure 4: Example Session-Sender test packet for SR-MPLS Policy
For end-to-end P2MP SR-MPLS Policy, STAMP Session-Sender test packets are transmitted with:
  Tree-SID of the P2MP SR-MPLS Policy
  IPv4 destination address selected from 127/8 range
  IPv4 TTL is set to 1

## Slide 9: STAMP Session-Reflector Test Packet
STAMP Session-Reflector reply test packet is sent using the IP/UDP information from the received test packet.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Reflector IPv4 or IPv6 Address .
. Destination IP Address = .
. Source IP Address from Received Test Packet .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Reflector .
. Destination Port = Source Port from Received Test Packet .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.3 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure 5: STAMP Session-Reflector Test Packet

## Slide 10: Performance Measurement Modes
Need to measure in-band one-way, two-way and round-trip delay metrics in SR networks
One-way Delay Measurement Mode
  Existing (default) behavior
Two-way Delay Measurement Mode
  STAMP Session-Reflector test packet sent “in-band” on reverse path
  Avoid per test session state on Session-Reflector
  Link: Use Control Code Sub-TLV in the Return Path TLV from the received test packet.
  E2E SR path: Use Segment List Sub-TLV in the Return Path TLV from the received test packet.
Round-trip Delay Measurement Mode
  STAMP Session-Sender test packet sent in loopback mode, carries the return path in the packet header

## Slide 11: ECMP Support for SR Path
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes
Sending STAMP test packets that can take advantage of the hashing function in forwarding plane
Existing forwarding mechanisms are applicable to test packets. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8)
    Identify intended actual destination node in “Destination Node Address TLV”
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 12: Example PM Metrics
Compute following example (one-way, two-way, round-trip) delay metrics:
  Minimum delay
  Maximum delay
  Average delay
  Delay variance
Compute following example loss metrics:
  Packet loss (i.e., synthetic packet loss)
  Direct measurement packet counters
  Session status succeeded/failed (i.e., measurement is active)

## Slide 13: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 14
Thank you