## Slide 1: Performance Measurement Using RFC 6374 with UDP Path for Segment Routing Networks
draft-gandhi-spring-rfc6374-srpm-udp-04
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)
Mach Chen - Huawei (mach.chen@huawei.com)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Updates Since IETF-104
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM)
    Links and End-to-end P2P/ P2MP SR Paths
    Applicable to SR-MPLS/SRv6 data planes
  No need to negotiate UDP port to bootstrap PM session - spirit of SR
    Stateless on egress node - spirit of SR
  Handle ECMP for SR Paths
  Scope:
  Use RFC 6374 defined probe message formats
  Use RFC 7876 (IP/UDP OOB return path) defined probe response messages
  User defined IP/UDP path for PM probe messages

## Slide 4: History of the Draft
Mar 2018
  Draft was published draft-gandhi-spring-udp-pm-00
July 2018
  Presented draft-gandhi-spring-udp-pm-01 at IETF 102 Montreal in SPRING WG
Nov 2018
  Presented draft-gandhi-spring-udp-pm-02 at IETF 103 Bangkok in SPRING and IPPM WGs
Feb 14, 2019
  Draft was renamed to draft-gandhi-spring-rfc6374-srpm-udp-00
Mar 2019
  Presented draft-gandhi-spring-rfc6374-srpm-udp-00 at IETF 104 Prague in SPRING WG

## Slide 5: Updates Since IETF-104 (Revision-00)
Updates:
  Add loopback measurement mode
  Reference for probe message processing rules
    TTL value, UDP Checksum and Router Alert
  Reference for example provisioning model
  Align with draft-gandhi-mpls-rfc6374-sr
    Return Path TLVs for SR
  Various editorial changes to address review comments
Open Items:
  None

## Slide 6: Next Steps
Welcome your comments and suggestions
Like to request for WG adoption

## Slide 7
Thank you

## Slide 8
Backup

## Slide 9: Probe Query Messages
IP/UDP path is defined for PM probe query messages for delay and loss measurements for SR links and end-to-end P2P and P2MP SR Paths.
Payload contains [RFC6374] defined message for DM or LM.
User-configured UDP port TBA1 is used for identifying DM probe packets.
User-configured UDP port TBD2 is used for identifying LM probe packets.
User-configured UDP port TBD3 is used for identifying Combined LM+DM probe packets.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Querier IPv4 or IPv6 Address .
. Destination IP Address = Responder IPv4 or IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Querier .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = Message as specified in RFC 6374 for DM, LM, LM/DM |
. .
+---------------------------------------------------------------+

## Slide 10: Probe Query for SR-MPLS and SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message for DM or LM or LM/DM Query with IP/UDP Header |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SR-MPLS Policy
For end-to-end performance delay/loss measurement of SR Policy, the probe query messages are sent on the SR Policy path with:
MPLS label stack for SR-MPLS Policy
SRv6 SRH [RFC 8754] with SID list for SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Querier IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH |
. <SID List> .
. .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Querier IPv6 Address .
. Destination IP Address = Responder IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Querier .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Message for DM or LM or LM/DM Query |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SRv6 Policy

## Slide 11: Probe Response Messages
Probe response messages can be sent in-band (two-way measurement) or out-of-band (one-way measurement) for SR links and SR Policies.
Use the information from the UDP Return Object (URO) TLV [RFC7876] from the received Probe query message payload, otherwise use the IP/UDP information (Source IP Address and Source UDP port) from the received Probe query message header.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Responder IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from Query .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Responder .
. Destination Port = Source Port from Query .
. .
+---------------------------------------------------------------+
| Message as specified in Section 3.2 of RFC 6374 for DM, or |
. Message as specified in Section 3.1 of RFC 6374 for LM, or .
. Message as specified in Section 3.3 of RFC 6374 for LM/DM .
. .
+---------------------------------------------------------------+
Figure: Probe Response Message
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Responder IPv4 or IPv6 Address .
. Destination IP Address = URO.Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Responder .
. Destination Port = URO.UDP-Destination-Port .
. .
+---------------------------------------------------------------+
| Message as specified in Section 3.2 of RFC 6374 for DM, or |
. Message as specified in Section 3.1 of RFC 6374 for LM, or .
. Message as specified in Section 3.3 of RFC 6374 for LM/DM .
. .
+---------------------------------------------------------------+
Figure: Probe Response Message Using URO from Probe Query

## Slide 12: Return Path TLV for Two-way Measurement
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Return Path Sub-TLVs |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Return Path TLV
Sub-TLV Types:
Type (value TBA1): SRv6 Segment List of the Reverse SR Path
Type (value TBA2): SRv6 Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
TLV is mandatory when carried in a probe query and if responder does not support, it MUST return Error 0x17: Unsupported Mandatory TLV Object
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Segment List Sub-TLV in Return Path TLV

## Slide 13: Authenticated Mode
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type TBA4 | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Comp.MBZ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| HMAC (16 octets) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Sequence Number TLV - Authenticated Mode
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type TBA3 | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Sequence Number TLV - Unauthenticated Mode
Define Sequence Number TLV for Probe Query and Response messages.
Useful when some probe query messages are lost, or they arrive out of order.
Used for authentication of probe messages.

## Slide 14: ECMP Support for SR Path
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8)
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 15
Thank you