## Slide 1: Enhanced Performance Measurement and Liveness Monitoring in Segment Routing Networks
draft-gandhi-spring-sr-enhanced-plm-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Navin Vaghamshi - Reliance (Navin.Vaghamshi@ril.com)
Moses Nagarajah - Telstra (Moses.Nagarajah@team.telstra.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Performance Measurement & Liveness Monitoring in SR networks
    End-to-end P2P/P2MP SR Paths
    Applicable to SR-MPLS/SRv6 data planes
    Support ECMP SR paths
  Running single protocol for liveness detection and performance measurement in SR networks
    Simplify deployment and reduce operational complexity
  No endpoint dependency
    Stateless on endpoint (e.g. endpoint unaware of the probe protocol)
    Higher scale and faster detection interval (e.g. packets not punted from fast-path)
  Scope:
  RFC 5357 (TWAMP Light) defined probe messages
  RFC 8762 (STAMP) defined probe messages
  User-configured IP/UDP path for probe messages

## Slide 4: Liveness Monitoring of SR Policy
Liveness monitoring for SR Policy uses PM probes (TWAMP Light/STAMP delay measurement messages) in Loopback Mode
Probe messages sent using Segment List(s) of the SR Policy Candidate Path(s)
Probe messages are not punted on the remote node (endpoint/reflector)
Return path can be IP or SR
Liveness failure is notified when consecutive N number of probe messages are not received back at the sender
+-------+ t1 Probe +-------+
| | - - - - - - - - - - | |
| R1 |--------------------|| R5 |
| |<- - - - - - - - - - | |
+-------+ t4 Return Probe +-------+
Sender Reflector Endpoint
(Simply Forward)
Figure: Loopback Mode

## Slide 5: Enhanced Liveness Monitoring of SR Policy
Use PM probes in loopback mode enabled with network programming function
  The network programming function optimizes the "operations of punt, add receive timestamp and inject the probe packet" on the reflector node
The endpoint node adds the receive timestamp in the payload of the received TWAMP Light or STAMP probe message without punting the probe message
  Only add the receive timestamp if the source address in the probe message matches the local node address
Liveness failure is notified when consecutive N number of probe messages are not received back at the sender
Delay metrics are notified when consecutive N number of probe messages have delay values exceed the configured thresholds
+-------+ t1 Probe t2 +-------+
| | - - - - - - - - - - | |
| R1 |--------------------|| R5 |
| |<- - - - - - - - - - | |
+-------+ Return Probe +-------+
Sender Reflector Endpoint
(Timestamp,
Pop and Forward)
Figure: Loopback Mode Enabled with Network Programming

## Slide 6: TWAMP Light Probe Message
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
~ Padding ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Probe Message Format
Enhanced Loopback Mode
Sender adds the Transmit Timestamp
Reflector adds the Receive Timestamp at fixed offset locally provisioned (consistently in the network)
  For TWAMP Light packets, it is at offset-byte 16 from the start of the payload
Sender Sequence Number, Sender Timestamp, Sender Error Estimate and Sender TTL in the TWAMP Light messages are not used
  Reflector does not copy them

## Slide 7: STAMP Probe Message
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | Padding |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Probe Message Format
Enhanced Loopback Mode
Sender adds the Transmit Timestamp
Reflector adds the Receive Timestamp at fixed offset locally provisioned (consistently in the network)
  For STAMP packets, it is at offset-byte 16 from the start of the payload
Sender Sequence Number, Sender Timestamp, Sender Error Estimate and Sender TTL in the STAMP messages are not used
  Reflector does not copy them

## Slide 8: SR-MPLS with Timestamp Label
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp Label (TBA1) | TC |S| TTL |
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Endpoint IPv4 or IPv6 Address .
. Destination IP Address = Sender IPv4 or IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload as defined in Section 4.2.1 of RFC 5357 | |
| Payload as defined in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure 5: Probe Message Header for SR-MPLS with Timestamp Label
Timestamp Label (TBA1) allocated by IANA from Extended Special-Purpose MPLS Label Values
  Used for Timestamp, Pop and Forward network programing function
Source and Destination Addresses are swapped - represent Reverse direction path
Optionally, Reverse direction SR path label stack can follow the Timestamp Label

## Slide 9: ECMP Support for SR Paths
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages:
  For IPv4
    Destination addresses in IPv4 header (e.g. 127/8) when return path is SR-MPLS
  For IPv6
    Destination addresses in IPv6 header (e.g. ::FFFF:127/104) when return path is SRv6
    Flow label in IPv6 header

## Slide 10: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Network Programming Label
Measurement Protocol / \ Timestamp Offset
PLM Type / \ Timestamp Format
LB or Enhanced LB / \
Authentication Mode & Key / \
Network Programming Label / \
Timestamp Format / \
/ \
v v
+-------+ +-------+
| | SR Path | |
| R1 |============| R5 |
| | | |
+-------+ +-------+
Sender Reflector

## Slide 11: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 12
Thank you

## Slide 13: Backup

## Slide 14: SRv6 with Timestamp and Forward Function
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Endpoint IPv6 Address .
. Destination IP Address = Sender IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| SRH |
. <Segment List> .
. END.TSF with Target SID .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload as defined in Section 4.2.1 of RFC 5357 | |
| Payload as defined in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure: Probe Message Header for SRv6 with Endpoint Function
Endpoint Function END.TSF is defined for Timestamp and Forward
Source and Destination Addresses are swapped for the Reverse direction path in the inner IPv6 header
Optionally, Reverse direction SR path can be carried in SRH

## Slide 15
Thank you

## Slide 16: Enhanced Loopback Mode for SR-MPLS Policy - IP/UDP Return Path
Probe Query
Probe Reply
2 PE
3
4 PE
24134
TS LABEL TBA1
IPv4/UDP Source: PE4 Destination: PE2 RFC 5357
Payload RFC 5357 Timestamp1
TS LABEL TBA1
IPv4/UDP Source: PE4 Destination: PE2 RFC 5357
Payload RFC 5357 Timestamp1
IPv4/UDP Source: PE4 Destination: PE2 RFC 5357
Payload RFC 5357 Timestamp1, Timestamp2
IPv4/UDP Source: PE4 Destination: PE2 RFC 5357
Payload RFC 5357 Timestamp1, Timestamp2

## Slide 17: Enhanced Loopback Mode for SR-MPLS Policy - SR Return Path
Probe Query
Probe Reply
2 PE
3
4 PE
24134
TS LABEL TBA1
NODE-SID 16002
IPv4/UDP Source: PE4 Dest: PE2 or 127/8 RFC 5357
Payload RFC 5357 Timestamp1
TS LABEL TBA1
NODE-SID 16002
IPv4/UDP Source: PE4 Dest: PE2 or 127/8 RFC 5357
Payload RFC 5357 Timestamp1
NODE-SID 16002
IPv4/UDP Source: PE4 Dest: PE2 or 127/8 RFC 5357
Payload RFC 5357 Timestamp1, Timestamp2
NODE-SID 16002
IPv4/UDP Source: PE4 Dest: PE2 or 127/8 RFC 5357
Payload RFC 5357 Timestamp1, Timestamp2

## Slide 18
Thank you