## Slide 1: Simple TWAMP (STAMP) Extensions for Segment Routing Networks
draft-gandhi-ippm-stamp-srpm-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Summary of Extensions
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Support Delay and synthetic Loss Measurement
  Support stand-alone direct-mode Loss Measurement
  Scope:
  STAMP [RFC 8762]
  STAMP TLVs [draft-ietf-ippm-stamp-option-tlv]

## Slide 4: STAMP - Summary of PM Drafts
draft-gandhi-spring-stamp-srpm
Defines procedures for delay, synthetic loss and direct-mode loss measurements
  For Links and end-to-end SR Paths for SR-MPLS and SRv6 data planes
draft-gandhi-ippm-stamp-srpm
Defines extensions for STAMP for Segment Routing
  Defines Session-Sender Control Code field for in-band response request
  Defines stand-alone direct-mode loss measurement query and response messages
  Defines TLVs to carry Destination Node Address and Return Path

## Slide 5: History of the Draft
Feb 2019
  Draft was published - draft-gandhi-spring-twamp-srpm-00
Mar 2019
  Presented draft-gandhi-spring-twamp-srpm-00 at IETF 104 Prague in SPRING WG
May 2019
  Added STAMP TLV for Return Path
July 2019
  Presented draft-gandhi-spring-twamp-srpm-01 at IETF 105 Montreal in IPPM WG
    Slide 9 Titled - Applicability of STAMP
Nov 2019
  SPRING Chairs announced in the meeting the agreement with IPPM chairs to progress the draft in SPRING WG
  Presented draft-gandhi-spring-twamp-srpm-04 at IETF 106 Singapore in SPRING WG
Mar 2020
  Moved STAMP support to draft-gandhi-spring-stamp-srpm-00
  Keep TWAMP Light support as informational in draft-gandhi-spring-twamp-srpm-08
Jul 2020
  Presented draft-gandhi-spring-stamp-srpm-01 at IETF 108 in SPRING and IPPM WG
October 2020
  Split draft into draft-gandhi-spring-stamp-srpm-03 and draft-gandhi-ippm-stamp-srpm-00

## Slide 6: STAMP - Session-Sender Control Code Field
In a Query: Session-Sender Control Code
0x0: Out-of-band Response Requested.
This is the existing behavior.
0x1: In-band Response Requested.
Indicates that this query has been sent over a bidirectional path and the probe response is required over the same path in reverse direction.
0x2: No Response Requested.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Sequence Number | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Timestamp | | | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ |Se Control Code|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| MBZ (24 octets) |
| |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Sender Control Code in STAMP DM Message
With this, the Session-Reflector node does not require any additional state for PM

## Slide 7: STAMP - Stand-alone Direct-mode LM Message Format
Stand-alone Direct-mode Loss Measurement (LM) query and response messages defined
  Hardware efficient counter-stamping
    Well-known locations for transmit and receive traffic counters
  Stand-alone LM message, not tied to DM
Direct-mode LM message format is also defined for authenticated mode
User-configured destination UDP Port2 is used for identifying direct-mode LM probe packets
Does not modify existing STAMP (which is for DM) procedure as different destination UDP port is used for direct-mode LM
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port2 for Loss Measurement.
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved | Block Number | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved |Sender Block Nu| MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 8: STAMP - Destination Node Address TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Address Family |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Address ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Node Address TLV Format
Destination Node Address TLV (value TBA1):
Indicates the address of the intended recipient node of the query message.
The Session-Reflector node MUST NOT send response if it is not the intended destination node of the query.
Useful when query is sent with 127/8 destination address.

## Slide 9: STAMP - Return Path TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type = TBA2 | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Return Path Sub-TLVs |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Return Path TLV
Return Path TLV (value TBA2):
Sub-TLVs Types:
Type (value 1): Return Address. Target node address of the response; different than the Source Address in the query
Type (value 2): SR-MPLS Label Stack of the Reverse SR Path
Type (value 3): SR-MPLS Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
Type (value 4): SRv6 Segment List of the Reverse SR Path
Type (value 5): SRv6 Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Segment List Sub-TLV in Return Path TLV

## Slide 10: draft-gandhi-ippm-stamp-srpm - Review Comments
Draft status:
  Draft defines extensions for STAMP (is not a new protocol)
  Update RFC 8762 due to new field (control code) in the message
Extensions are not specific to SR, document should be renamed
Does not introduce any new security issue with this draft
Editorial
  Define Abbreviations (BSID, SRH, HMAC-SHA)
  Use Session-Sender, Session-Reflector terms
  Show entire test packet with session-sender control code field
  Indicate packet loss is direct-mode loss
  Move Receive Counter and other Response message fields to Section 4.1 from 3.2
    Explain how the counters and sequence numbers are used to do loss measurement
Extend ICMP for direct-mode loss measurement – out of scope

## Slide 11: draft-gandhi-spring-stamp-srpm - Review Comments
Destination UDP port used has zero UDP checksum with IPv6 header
  Add Reference for RFC 6936 in Security Section
Add references for well-known terms “Link”, “SR Path”, and “Congruent paths”
Add reference for Yang data model draft in provisioning model section
Liveness is to compute “connection loss” performance metric
  Similar to the widely deployed synthetic packet loss metric
Editorial
  Indicate packet loss is direct-mode loss
  Use test packet term for query message
  H/W timestamps required -> H/W timestamps recommended
  IPv6 address ::1/128 or ::FFFF:127/104
  Clarify - Section 4.1.4.2 and 4.2.2.2 depict the packet format with word “as needed” for inner IP Header
  Different UDP destination port when running authenticated and unauthenticated sessions simultaneously

## Slide 12: Next Steps
Welcome your comments and suggestions
In IPPM WG adoption poll

## Slide 13
Thank you