## Slide 1: Performance Measurement Using UDP Path for Segment Routing Networks
draft-gandhi-spring-rfc6374-srpm-udp-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)
Mach Chen - Huawei (mach.chen@huawei.com)
Sagar Soni - Cisco Systems (sagsoni@cisco.com)
Patrick Khordoc - Cisco Systems (pkhordoc@cisco.com)
Zafar Ali - Cisco Systems (zali@cisco.com) Pier Luigi Ventre - CNIT (pierluigi.ventre@cnit.it)

## Slide 2: Agenda
Requirements and Scope
Updates Since IETF-104
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM) for SR links and end-to-end P2P/ P2MP SR Policies
    Applicable to SR-MPLS/SRv6 data planes
  No need to bootstrap PM session (e.g. to negotiate UDP port) - spirit of SR
    Stateless on egress node - spirit of SR
  Handle ECMP for SR Policies
  Scope:
  Use RFC 6374 defined probe message formats
  Use RFC 7876 (IP/UDP OOB return path) defined probe response messages
  User defined IP/UDP path for PM probe messages

## Slide 4: Updates Since IETF-104 (Revision-00)
Updates:
  Add loopback measurement mode
  Elaborate on message processing rules (e.g. TTL value, UDP Checksum and Router Alert)
  Show example provisioning model
  Add details for P2MP SR Policy
  Move SR-MPLS Return Path TLV and Block Number TLV to SR-MPLS draft
    They are not related to UDP path extensions and belong to the base MPLS draft
  Various editorial changes to address review comments
    Change the term “in-band probes” with “probes sent on congruent path with data traffic”
Open Items:
  None

## Slide 5: History of the Draft
Mar 2018
  Draft was published draft-gandhi-spring-udp-pm
Nov 2018
  Presented revison-02 at IETF 103 Bangkok in SPRING and IPPM WGs
Feb 14, 2019
  Draft was renamed to draft-gandhi-spring-rfc6374-srpm-udp
Mar 2019
  Presented revision-00 at IETF 104 Prague in SPRING WG

## Slide 6: Next Steps
Welcome your comments and suggestions
Multiple implementations of RFC 6374 already exist
Like to request for WG adoption

## Slide 7
Thank you