## Slide 1: Segment Routing with MPLS Data Plane Encapsulation for In-situ OAM Data
draft-gandhi-mpls-ioam-sr-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Zafar Ali - Cisco Systems (zali@cisco.com)
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Frank Brockners - Cisco Systems (fbrockne@cisco.com)
Bin Wen - Comcast (Bin_Wen@cable.comcast.com)
Voitek Kozak - Comcast (Voitek_Kozak@comcast.com)
Sagar Soni - Cisco Systems (sagsoni@cisco.com)
Patrick Khordoc - Cisco Systems (pkhordoc@cisco.com)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Updates Since IETF-104
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Transport In-situ OAM (IOAM) data fields with SR-MPLS Encapsulation
    OAM information (e.g. timestamps) carried by data traffic
  Scope:
  Using data fields defined in draft-ietf-ippm-ioam-data, draft-ioamteam-ippm-ioam-direct-export and draft-ietf-ippm-ioam-flags
  Edge-to-edge IOAM
  Hop-by-hop IOAM

## Slide 4: History of the Draft
Oct 2018
  Draft was first published draft-gandhi-spring-ioam-sr-mpls
Nov 2018 and March 2019
  Draft was discussed in IPPM WG meetings
July 2019
  Presented revision-01 at IETF 105 Montreal in SPRING and MPLS WGs
Oct 2019
  Chairs agreed to progress the work in MPLS WG
  Draft renamed to draft-gandhi-mpls-ioam-sr

## Slide 5: Updates Since IETF-104 (Revision-01)
Updates:
  Added mechanisms to avoid incorrect IP header based hashing
    Uses flow-label based mechanisms
  Added example with Path Segment Identifier
  Various editorial changes to address review comments
  Open Items:
    Add procedure for hop-by-hop IOAM

## Slide 6: E2E IOAM Data Field Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM Indicator Label TBA1 | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| IOAM-Type | IOAM HDR LEN | RESERVED | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: E2E IOAM encapsulation in MPLS Header

## Slide 7: E2E IOAM Data Field Encapsulation with Flow Label in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM and Flow Indicator Label TBA2 | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 0| Flow label | RESERVED |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| IOAM-Type | IOAM HDR LEN | RESERVED | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: E2E IOAM encapsulation with Flow Label in MPLS Header

## Slide 8: E2E IOAM Procedure
The encapsulating node inserts the IOAM Indicator Label and one or more IOAM data field(s) in the MPLS header.
The decapsulating node "forwards and punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.

## Slide 9: E2E Indicator Label Allocation Methods
Label assigned by IANA with values TBA1 and TBA2
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on both encapsulating and decapsulating nodes
Label allocated by the decapsulating node
  Signaling mechanism used to convey the label to all encapsulating nodes

## Slide 10: HbH IOAM Data Field Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM Indicator Label TBA3 | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| IOAM-Type | IOAM HDR LEN | RESERVED | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: HbH IOAM encapsulation in MPLS Header

## Slide 11: HbH IOAM Data Field Encapsulation with Flow Label in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM and Flow Indicator Label TBA4 | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 0| Flow label | RESERVED |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| IOAM-Type | IOAM HDR LEN | RESERVED | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: HbH IOAM encapsulation with Flow Label in MPLS Header

## Slide 12: Next Steps
Procedure for hop-by-hop IOAM
Welcome your comments and suggestions
Draft to progress in MPLS WG
  IANA Code points allocated by MPLS WG
  Keep SPRING WG in the loop for SR use-cases
  Inform SPRING and IPPM about the milestones

## Slide 13
Thank you