## Slide 1: Simple Two-Way Direct Loss Measurement Procedure
draft-gandhi-ippm-simple-direct-loss-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Direct Loss Measurement (DLM) for accurate data packet loss
  Support Alternate-Marking Method (AMM) [RFC 8321]
  High scale for number of sessions and faster packet loss detection interval
    Support hardware implementation
Goals:
  Avoid provisioning and maintaining sessions on Session-Reflector
  Avoid control protocol for signaling dynamic parameters
  Scope:
  Follow STAMP [RFC 8762] approach

## Slide 4: Alternate Marking Method for Packet Loss
RFC 8321 - Alternate-Marking Method for Passive and Hybrid Performance Monitoring
RFC 8957 - Synonymous Flow Label Framework
A: packet with A coloring
B: packet with B coloring
| | | | |
| | Traffic Flow | |
------------------------------------------------------------------->
BBBBBBB AAAAAAAAAAA BBBBBBBBBBB AAAAAAAAAAA BBBBBBBBBBB AAAAAAA
------------------------------------------------------------------->
... | Block 5 | Block 4 | Block 3 | Block 2 | Block 1
| | | | |
Figure 2: Traffic Coloring

## Slide 5: Case 1. STAMP Test Packets with Direct Measurement TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| |
+ +
| MBZ (28 octets) |
+ +
| |
| |
+ +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: STAMP Session-Sender Test Packet Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ses-Sender TTL | MBZ2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: STAMP Session-Reflector Test Packet Format
110th IETF Online
5

## Slide 6: Case 2. Direct Loss Measurement Probe Packet for Data Packet Loss Detection
Base Direct Loss Measurement probe packet defined
  Hardware efficient counter updating
    Well-known locations for traffic counters
  Block number of the counters for alternate-marking method [RFC 8321]
  Traffic class of the counters for per class packet loss
  DLM probe packet is also defined for authenticated mode
User-configured destination UDP Port is used for identifying DLM probe packets (different than port 862 and the one used by STAMP)
Sequence Number allows to monitor DLM session status, out of order probe packets and probe packet drops
Flags
  X set to 1 for 64-Bit Counter, set to 0 for 32-Bit Counter
  B set to 1 for Byte Counter, set to 0 for Packet Counter
  T set to 1 for Sender-DSCP scoped Counter
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter (C3) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B|T| DSCP | Block Number| DSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter (C2) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Counter (C1) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|FLAGS| Ses-DSCP |Ses-Block Num| MBZ (2 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ses-Sender TTL| MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Reflector Direct Loss Measurement Probe Packet

## Slide 7: Direct Measurement TLV vs. Direct Loss Measurement Probe Packet
Attributes | Case 1. STAMP Direct Measurement TLV | Case 1a. Define New STAMP Direct Measurement TLV? | Case 2. Direct Loss Measurement Probe Packet
Need to write timestamp (clock sync needed for one-way delay) | Yes | Yes | No
Counter at fixed location in the probe packet for hardware-based counter update | No (TLV-based) | No (TLV-based) | Yes
Reply probe packets with counter at fixed location for hardware-based counter update | No | No | Yes
Need to scan for DM TLV in each received probe packet on Session-Reflector in hardware (there can be multiple TLVs) | Yes | Yes | No
32-bit and 64-bit Byte counters | No | Yes | Yes
64-bit packet counters | No | Yes | Yes
Alternate-marking method packet loss - using block number for counters (out-of-order data packet support) | No | Yes | Yes
Per Traffic Class Counters | No | Yes | Yes

## Slide 8: Data Packet Loss Calculation
Using the Counters C1, C2, C3 and C4 as per reference topology, from the nth and (n-1)th Direct Loss Measurement probe packets.
  Transmit Loss TxL[n-1, n] = (C1[n] - C1[n-1]) - (C2[n] - C2[n-1])
  Receive Loss RxL[n-1, n] = (C3[n] - C3[n-1]) - (C4[n] - C4[n-1])
When using Alternate-Marking Method, all Counters used for the loss calculation belongs to the same Block Number, as described in Section 3.1 of [RFC8321].
C1 C2
/ \
+-------+ DLM Probe Packet +-------+
| | - - - - - - - - - - - ->| |
| R1 |=========================| R3 |
| |<- - - - - - - - - - - - | |
+-------+ DLM Reply Probe Packet +-------+
\ /
C4 C3
Session-Sender Session-Reflector
Reference Topology

## Slide 9: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 10
Thank you