## Slide 1: Simple TWAMP (STAMP) Extensions for Segment Routing Networks
draft-gandhi-ippm-stamp-srpm-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
Summary of Extensions
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Support in-band Performance Measurement for links and SR paths
Goals:
  Avoid provisioning sessions on Session-Reflector for stateless mode
  Avoid control-channel signaling for dynamic parameters
  Very high scale for number of sessions and faster detection interval
    Support hardware implementation
  Scope:
  STAMP [RFC 8762]
  STAMP Extensions [RFC8972]

## Slide 4: STAMP Session-Sender Control Code Field
Session-Sender Control Code (8-bit) Flags:
0x0: Existing default behavior as defined in RFC 8762.
0x1: In-band Reply Requested.
Indicates that this test packet has been sent over a bidirectional path and the reply is required in-band over the same link in the reverse direction.
0x2: No Reply Requested.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Sequence Number | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Timestamp | | | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ | Control Code |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| MBZ (24 octets) |
| |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Control Code in Session-Sender Test Packet – Unauthenticated

## Slide 5: STAMP Session-Sender Control Code Field - Usage
Two-way delay measurement mode for links
  Reflector needs to send reply on the same link (symmetric delay on forward and reverse link)
  Link can be Virtual, LAG or LAG member
Avoid provisioning each session (session id, source-address) on Session-Reflector (can have an order of 1K links)
  Stateless mode of STAMP Session-Reflector as defined in RFC 8762

## Slide 6: STAMP Return Path TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type = TBA2 | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Return Path Sub-TLV |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Return Path TLV
Return Path TLV (value TBA2) to carry one Sub-TLV for return path:
Sub-TLVs Types:
Type (value 1): Return Address. Destination node address for the reply; different than the Source Address in the test packet
Type (value 2): SR-MPLS Label Stack of the Return SR Path
Type (value 3): SR-MPLS Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
Type (value 4): SRv6 Segment List of the Return SR Path
Type (value 5): SRv6 Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Segment List Sub-TLV in Return Path TLV

## Slide 7: STAMP Return Path TLV - Usage
For SR path, reply test packet may need to be sent on the reverse SR Policy
Bidir SR Path (forward and reverse) dynamically computed using CSPF by the head-end node
  Path can change often based on topology change, link/node failure in the network, etc.
No signaling in SR, possible to use PCE
Avoid dynamic state on Session-Reflector node to store reverse paths for each session (each session-id, source-address)
  Order of 10K SR Policy (that can have active and standby candidate-path and each can have multiple segment-lists)

## Slide 8: STAMP Destination Node Address TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Address Family |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Address ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Destination Node Address TLV Format
Destination Node Address TLV (value TBA1):
Indicates the address of the intended destination node of the Session-Sender test packet.
The Session-Reflector node MUST NOT send reply if it is not the intended destination node of the test packet.
Useful when test packet is sent with 127/8 destination address (e.g. sweeping ECMP paths).

## Slide 9: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 10
Thank you