## Slide 1: Enhanced Performance and Liveness Monitoring in Segment Routing Networks
draft-gandhi-spring-sr-enhanced-plm-04
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Navin Vaghamshi - Reliance (Navin.Vaghamshi@ril.com)
Moses Nagarajah - Telstra (Moses.Nagarajah@team.telstra.com)
Richard Foote - Nokia (footer.foote@nokia.com)

## Slide 2: Agenda
Requirements and Scope
History and Summary of Updates
Review of the Procedure
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Performance and Liveness Monitoring (PLM) in SR networks
    End-to-end SR paths
    Applicable to SR-MPLS/SRv6 data planes
  Running single protocol in SR networks
    Simplify implementations and reduce development cost
    Simplify deployment and reduce operational complexity
  No Session-Reflector dependency
    Session-Reflector unaware of the monitoring protocol
      State is in the test packet - spirit of SR
    Higher test session scale and faster failure detection interval
  Scope:
  Leverage RFC 8762 (Simple TWAMP (STAMP)) hardware implementation

## Slide 4: History of the Draft
March 2020
  Draft was published
April 2020
  Presented version 00 in IETF 107 Virtual MPLS WG Meeting
July 2020
  Presented version 02 in IETF 108 Online SPRING WG meeting
September 2020
  Presented version 02 in MPLS WG Interim meeting

## Slide 5: Updates Since IETF-108 (Version-02)
Updates:
  Updated terminology
    test packets, consistent terms for MPLS Timestamp Label and SRv6 Timestamp Endpoint
  Added authentication mode
  Added SRv6 Timestamp Endpoint function assignment and Node Capability section
  Added synthetic packet loss section
  Updated IANA section
  Various editorial changes
  Open Items:
    None

## Slide 6: Loopback Mode for SR Policy
PLM test packets in Loopback Mode
PLM test packets are transmitted for each Segment List(s) of the SR Policy Candidate Path(s)
PLM test packets are forwarded in fast-path just like data traffic on Session Reflector - not punted to slow-path
Session-Reflector is agnostic to the PLM protocol
Round-trip delay = (T4 - T1)
T1
/
+-------+ PLM Test Packet +-------+
| | - - - - - - - - - - - | |
| R1 |======================|| R3 |
| |<- - - - - - - - - - - | |
+-------+ Return Test Packet +-------+
\
T4
Session-Sender Session-Reflector
(Simply Forward)
Figure: PLM Loopback Mode

## Slide 7: Loopback Mode Enabled with Network Programming Function
PLM test packets transmitted in loopback mode enabled with network programming function
  The network programming function optimizes the "operations of punt and inject the test packet" on Session-Reflector
  As PLM test packets are forwarded in fast-path, higher session scale with faster failure detection interval is achieved
Session-Reflector adds receive timestamp at a specific location in the payload of the received test packet in fast-path
  Only adds the receive timestamp if the source address or destination address in the received test packet matches the local node address
  Ensure loopback PLM test packets return from the intended Session-Reflector
One-way delay = (T2 – T1)
T1 T2
/ \
+-------+ PLM Test Packet +-------+
| | - - - - - - - - - - - | |
| R1 |======================|| R3 |
| |<- - - - - - - - - - - | |
+-------+ Return Test Packet +-------+
\
T4
Session-Sender Session-Reflector
(Timestamp,
Pop and Forward)

## Slide 8: Example Provisioning Model
+------------+
| Controller |
+------------+
PLM Mode / \ Timestamp Label/SRV6 EP
LB or Enhanced Mode / \ Timestamp Offset
Timestamp Label/SRv6 EP / \ Timestamp Format
Timestamp Format / \
Missed Packet Count N / \
Delay Threshold/Count M / \
Packet Loss Threshold XofY / \
v v
+-------+ +-------+
| | | |
| R1 |===========| R3 |
| | | |
+-------+ +-------+
Session-Sender Session-Reflector
Figure: Example Provisioning Model
* Provisioned, Flooded/Signaled or IANA Allocated

## Slide 9: PLM Test Packet Formats
Leverage existing STAMP implementations in hardware
Session-Sender adds Transmit Timestamp (T1)
Session-Reflector adds Receive Timestamp (T2) at offset-byte location in payload, for example,
  offset-byte 16 from the start of the payload in unauthenticated mode, or
  offset-byte 32 from the start of the payload in authenticated mode, or
  locally provisioned location (consistently in the network)
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp (T1) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp (T2) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ (16 Octets) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
PLM Test Packet Format in Unauthentication Mode
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ (12 octets) |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp (T1) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ (4 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp (T2) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ (4 Octets) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| MBZ (48 octets) |
| |
| |
| |
| |
| |
| |
| |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
PLM Test Packet Format in Authentication Mode

## Slide 10: SR-MPLS with Timestamp Label
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Label(1) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ . . . . . . +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Label(n) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Extension Label (15) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Timestamp Label (TBA1 or TBA2) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | IP Header | . Source IP Address = Session-Reflector IPv4 or IPv6 Address . . Destination IP Address = Session-Sender IPv4 or IPv6 Address .
. .
+---------------------------------------------------------------+ | UDP Header | . Source Port = As chosen by Session-Sender . . Destination Port = As chosen by Session-Sender . . . +---------------------------------------------------------------+ | PLM Test Packet |
. . +---------------------------------------------------------------+
Example PLM Test Packet with Timestamp Label for SR-MPLS
Timestamp label (TBA1) is defined for Timestamp, Pop and Forward function
Reverse Path can be IP or SR-MPLS
Source and Destination Addresses are swapped that represent the Reverse direction path

## Slide 11: SRv6 with Timestamp Endpoint Function
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. End.TSF (TBA3 or TBA4) with Session-Reflector SID .
. .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Reflector IPv6 Address .
. Destination IP Address = Session-Sender IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = As chosen by Session-Sender .
. .
+---------------------------------------------------------------+
| PLM Test Packet |
. .
+---------------------------------------------------------------+
Example PLM Test Packet with Timestamp Endpoint Function for SRv6
Timestamp Endpoint Function End.TSF (TBA3) is defined for Timestamp and Forward and is carried with the Session-Reflector node SID
Reverse path can be IP
  Session-Reflector removes SRH
Reverse path can be SR
  Reverse direction SR path Segment-list carried in SRH
  Session-Reflector does not remove the SRH
Source and Destination Addresses are swapped that represent the Reverse direction path in the inner IPv6 header

## Slide 12: Performance Metric Notifications
Liveness success (success of heart beats) initially is notified as soon as one or more PLM return test packets are received at the Session-Sender
Liveness failure (loss of heart beats) is notified when consecutive N number of PLM return test packets are not received at the Session-Sender
Synthetic packet loss is notified when X number of PLM return test packets not received at the Session-Sender out of last Y PLM test packets transmitted (with configured XofY threshold)
Delay metrics are notified as an example, when consecutive M number of PLM test packets have delay values exceed the configured thresholds (absolute/percentage)

## Slide 13: Next Steps
Welcome your comments and suggestions
Requesting SPRING WG adoption

## Slide 14
Thank you

## Slide 15: Backup

## Slide 16: Loopback Mode with Timestamp and Forward for SR-MPLS Policy
PLM Test
Packet
PLM Return
Test Packet
2 PE
3
4 PE
24134
15
TS LABEL TBA1
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1
15
TS LABEL TBA1
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1, Timestamp2
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1, Timestamp2

## Slide 17
Thank you