## Slide 1: Performance Measurement Using Simple TWAMP for Segment Routing Networks
draft-gandhi-spring-stamp-srpm-05
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
Summary of Procedure
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Measurement
    Links and end-to-end P2P/P2MP SR paths
      Links include physical, virtual, LAG, LAG member links
    Applicable to SR-MPLS/SRv6 data planes
  Handle ECMP for SR paths
Goals:
  Avoid per session provisioning on STAMP Session-Reflector
  Avoid control-channel signaling for sessions
  Very high scale for number of sessions and faster detection interval
    Support hardware implementation
  Scope:
  STAMP [RFC 8762]
  STAMP Extensions [RFC8972]
  draft-gandhi-ippm-stamp-srpm

## Slide 4: Example Provisioning Model
+------------+
| Controller |
+------------+
/ \
Destination UDP Port / \ Destination UDP port
Authentication Mode & Key / \ Authentication Mode & Key
Delay Measurement Mode / \ Synthetic Loss Type
Timestamp Format / \
Synthetic Loss Type / \
/ \
v v
+-------+ +-------+
| | | |
| R1 |============| R3 |
| | | |
+-------+ +-------+
STAMP Session-Sender STAMP Session-Reflector

## Slide 5: Session-Sender Test Packet for Links
For links, the STAMP Session-Sender test packets are transmitted over the links using local and remote link addresses.
User-configured destination UDP port1 is used for STAMP test packets (also port 862)
TTL is set 1.
Applicable to physical, virtual, LAG, LAG member links
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port & 862 .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure 1: Session-Sender Test Packet for links

## Slide 6: STAMP Session-Sender Test Packet for SR-MPLS and SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Test Packet including IP/UDP Header from Figure 1 |
. .
+---------------------------------------------------------------+
Figure 2: Example Session-Sender test packet for SR-MPLS Policy
For end-to-end SR Policy, the STAMP Session-Sender test packets are transmitted on the SR Policy with:
  MPLS label stack of SR-MPLS Policy
  SRv6 SRH [RFC 8754] with Segment List of SRv6 Policy
    Using upper layer processing in SRv6 network programming
User-configured destination UDP port1 is used for STAMP test packets (also port 862)
TTL is set 255
Color only SR-MPLS Policy:
  Destination Address in 127/8 address
  TTL is set 1.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Session-Reflector IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port & 862 .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.2 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure 3: Example Session-Sender test packet for SRv6 Policy

## Slide 7: STAMP Session-Sender Test Packet for P2MP SR-MPLS Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Tree-SID | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Test Packet including IP/UDP Header from Figure 1 |
. .
+---------------------------------------------------------------+
Figure 4: Example Session-Sender test packet for SR-MPLS Policy
For end-to-end P2MP SR-MPLS Policy, the STAMP Session-Sender test packet is sent with:
  Tree-SID of the SR-MPLS Policy
IPv4 destination address set from 127/8 range
TTL is set 1

## Slide 8: STAMP Session-Reflector Test Packet
The STAMP reply test packet is sent using the IP/UDP information from the received test packet.
Link - Use Control Code from the received test packet if set.
SR path - Use Segment List from Return Path TLV if present in the received test packet.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Reflector IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from Test Packet .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Reflector .
. Destination Port = Source Port from Test Packet .
. .
+---------------------------------------------------------------+
| Payload = Test Packet specified in Section 4.3 of RFC 8762 |
. .
+---------------------------------------------------------------+
Figure 5: STAMP Session-Reflector Test Packet

## Slide 9: ECMP Support for SR Path
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending STAMP test packets that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to test packets. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8)
    Identify intended actual destination node in “Destination Node Address TLV”
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 10: Performance Measurement Modes
One-way Delay Measurement Mode
  Existing default behavior
Two-way Delay Measurement Mode
  STAMP test packet reply sent “in-band” on reverse path
    Link - Use Control Code from the received test packet
    SR path - Use Return Path TLV from the received test packet
Loopback Measurement Mode
  STAMP Session-Sender test packet carries the return path in the header

## Slide 11: Example PM Metrics
Compute following example delay metrics:
  Minimum delay
  Maximum delay
  Average delay
  Delay variance
Compute following example loss metrics:
  Synthetic packet loss (aka indirect-mode packet loss)
  Connectivity loss (aka liveness heart-beat failure detection)

## Slide 12: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 13
Thank you