## Slide 1: Segment Routing with MPLS Data Plane Encapsulation for In-situ OAM Data
draft-gandhi-mpls-ioam-sr-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Zafar Ali - Cisco Systems (zali@cisco.com)
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Frank Brockners - Cisco Systems (fbrockne@cisco.com)
Bin Wen - Comcast (Bin_Wen@cable.comcast.com)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Updates Since IETF-106
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Transport In-situ OAM (IOAM) data fields with SR-MPLS Encapsulation
    OAM information (e.g. timestamps) carried by data traffic
  Scope:
  Using data fields defined in:
    draft-ietf-ippm-ioam-data
    draft-ietf-ippm-ioam-direct-export
    draft-ietf-ippm-ioam-flags
  Edge-to-edge (E2E) IOAM
  Hop-by-hop (HbH) IOAM

## Slide 4: History of the Draft
Oct 2018
  Draft was first published draft-gandhi-spring-ioam-sr-mpls
Nov 2018 and March 2019
  Draft was discussed in IPPM WG meetings as part of the IOAM updates
July 2019
  Presented revision-01 at IETF 105 Montreal in SPRING and MPLS WGs
Oct 2019
  Chairs agreed to progress the work in MPLS WG
  Draft renamed to draft-gandhi-mpls-ioam-sr
Nov 2019
  Presented revision-00 at IETF 106 Singapore in MPLS WG

## Slide 5: Updates Since IETF-106 (Revision-00)
Updates:
  Added procedure for hop-by-hop IOAM
  Various editorial changes
  Open Items:
    None

## Slide 6: IOAM Data Field Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| IOAM-Type | IOAM HDR LEN | RESERVED | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM encapsulation in MPLS Header

## Slide 7: IOAM Indicator Label
“IOAM Indicator Label” is used to indicate the presence of the IOAM data fields in the MPLS header.
Separate Label values are used for edge-to-edge and hop-by-hop IOAM:
  Edge-to-edge TBA1
  Hop-by-hop TBA3

## Slide 8: IOAM Data Field Encapsulation with Flow Label in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM and Flow Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 0| Flow label | Block Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| IOAM-Type | IOAM HDR LEN | RESERVED | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM encapsulation with Flow Label in MPLS Header

## Slide 9: IOAM and Flow Indicator Label
“IOAM and Flow Indicator Label” is used to indicate the presence of the IOAM data fields with Flow Label in the MPLS header.
Separate Label values are used for edge-to-edge and hop-by-hop IOAM:
  Edge-to-edge TBA2
  Hop-by-hop TBA4
Protocol value 0000b allows to avoid incorrect IP header based hashing over ECMP paths.
Flow Label identifies the traffic flow that can be used for IOAM purpose.
Block Number can be used to aggregate the IOAM data collected in data plane, e.g. compute measurement metrics for each block of a flow.

## Slide 10: Edge-to-edge IOAM Procedure
The encapsulating node inserts an edge-to-edge Indicator Label and one or more IOAM data field(s) in the MPLS header.
The decapsulating node for edge-to-edge IOAM "forwards and punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node for edge-to-edge IOAM also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.

## Slide 11: E2E Indicator Label Allocation Methods
Label assigned by IANA with values TBA1 and TBA2
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating and decapsulating nodes
The label allocated by the decapsulating node
  Signaling mechanism used to convey the label to all encapsulating nodes

## Slide 12: Hob-by-hop IOAM Procedure
The encapsulating node inserts a hop-by-hop Indicator Label and one or more IOAM data field(s) in the MPLS header.
The transit node for hop-by-hop IOAM "forwards and punts the timestamped copy" of the data packet including IOAM data field(s).
The decapsulating node for hop-by-hop IOAM "forwards and punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node for hop-by-hop IOAM also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.

## Slide 13: HbH Indicator Label Allocation Methods
Label assigned by IANA with values TBA3 and TBA4
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating, transit and decapsulating nodes

## Slide 14: Next Steps
Welcome your comments and suggestions

## Slide 15
Thank you

## Slide 16: WG Co-ordination Plan
Draft to progress in MPLS WG
  IANA code-points allocated by MPLS WG
Keep SPRING WG in the loop for SR aspects
  Inform SPRING WG about the milestones (adoption, Last Call)
Inform IPPM WG about the milestones (adoption, Last Call) as IOAM base work is done in IPPM