## Slide 1: Simple Two-Way Direct Loss Measurement Procedure
draft-gandhi-ippm-simple-direct-loss-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Direct Loss Measurement (DLM) for accurate data packet loss
  Support Alternate-Marking Method (AMM) [RFC 8321]
  High scale for number of sessions and faster packet loss detection interval
    Support hardware implementation
Goals:
  Avoid provisioning and maintaining sessions on Session-Reflector
  Avoid control protocol for signaling dynamic parameters
  Scope:
  Follow STAMP [RFC 8762] approach

## Slide 4: Alternate Marking Method for Packet Loss
RFC 8321 - Alternate-Marking Method for Passive and Hybrid Performance Monitoring
RFC 8957 - Synonymous Flow Label Framework
A: packet with A coloring
B: packet with B coloring
| | | | |
| | Traffic Flow | |
------------------------------------------------------------------->
BBBBBBB AAAAAAAAAAA BBBBBBBBBBB AAAAAAAAAAA BBBBBBBBBBB AAAAAAA
------------------------------------------------------------------->
... | Block 5 | Block 4 | Block 3 | Block 2 | Block 1
| | | | |
Figure 2: Traffic Coloring

## Slide 5: 1. STAMP Test Packets with Direct Measurement TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| |
+ +
| MBZ (28 octets) |
+ +
| |
| |
+ +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Sender Test Packet Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ses-Sender TTL | MBZ2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Reflector Test Packet Format
110th IETF Online
5

## Slide 6: 2. Direct Loss Measurement Probe Packet for Data Packet Loss Detection
Base Direct Loss Measurement probe packet defined
  Hardware efficient counter updating
    Well-known locations for traffic counters
  Block number of the counters for alternate-marking method [RFC 8321]
  Traffic class of the counters for per class packet loss
  DLM probe packet is also defined for authenticated mode
User-configured destination UDP Port is used for identifying DLM probe packets (different than port 862 and the one used by STAMP)
Sequence Number allows to monitor DLM session status
Flags
  X set to 1 for 64-Bit Counter, set to 0 for 32-Bit Counter
  B set to 1 for Byte Counter, set to 0 for Packet Counter
  T set to 1 for Sender-DSCP scoped Counter
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter (C3) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B|T| DSCP | Block Number| DSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter (C2) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Counter (C1) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|FLAGS| Ses-DSCP |Ses-Block Num| MBZ (2 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ses-Sender TTL| MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Reflector Direct Loss Measurement Probe Packet

## Slide 7: Direct Measurement TLV vs. Direct Loss Measurement Probe Packet
Attributes | 1. Direct Measurement TLV | Define New Direct Measurement TLV? | 2. Direct Loss Measurement Probe Packet
Need to write timestamp (clock sync needed for one-way delay) | Yes | Yes | No
Counter at fixed location in the probe packet for hardware counter writing | No (TLV-based) | No (TLV-based) | Yes
Reply probe packets with counter at fixed location for hardware counter-stamping | No | No | Yes
Need to scan for DM TLV in each received probe packet on Session-Reflector in hardware (there can be multiple TLVs) | Yes | Yes | No
32-bit and 64-bit Byte counters | No | Yes | Yes
64-bit packet counters | No | Yes | Yes
Alternate-marking method packet loss - using block number for counters (out-of-order data packet support) | No | Yes | Yes
Per Traffic Class Counters | No | Yes | Yes

## Slide 8: Data Packet Loss Calculation
Using the Counters C1, C2, C3 and C4 as per reference topology, from the nth and (n-1)th Direct Loss Measurement probe packets.
  Transmit Loss TxL[n-1, n] = (C1[n] - C1[n-1]) - (C2[n] - C2[n-1])
  Receive Loss RxL[n-1, n] = (C3[n] - C3[n-1]) - (C4[n] - C4[n-1])
When using Alternate-Marking Method, all Counters used for the loss calculation belongs to the same Block Number, as described in Section 3.1 of [RFC8321].
C1 C2
/ \
+-------+ DLM Probe Packet +-------+
| | - - - - - - - - - - - ->| |
| R1 |=========================| R3 |
| |<- - - - - - - - - - - - | |
+-------+ DLM Reply Probe Packet +-------+
\ /
C4 C3
Session-Sender Session-Reflector
Reference Topology

## Slide 9: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 10
Thank you