## Slide 1: Simple TWAMP (STAMP) Extensions for Direct Measurement
draft-gandhi-ippm-stamp-direct-loss-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
Summary of Extensions
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Support stand-alone Direct Measurement for accurate data packet loss
  Very high scale for number of sessions and faster detection interval
    Support hardware implementation
Goals:
  Avoid per session provisioning on Session-Reflector
  Avoid control protocol for test sessions
  Scope:
  STAMP [RFC 8762]

## Slide 4: Stand-alone Direct Measurement Test Packet for Packet Loss
Stand-alone Direct Measurement test packet defined
  Hardware efficient counter-stamping
    Well-known locations for transmit and receive traffic counters
  Block number of the counters for alternate marking method [RFC 8321]
  Traffic class of the counters for per class packet loss
Direct Measurement test packet is also defined for authenticated mode
User-configured destination UDP Port2 is used for identifying direct measurement test packets
Does not modify the existing STAMP procedure as different destination UDP port is used for direct measurement test packets
  Other than Timestamp vs. Counter in the test packet, the protocol is same as STAMP
Sequence Numbers allow to detect test packet loss, and connectivity loss
Flags
  X set to 1 for 64-Bit Counter, set to 0 for 32-Bit Counter
  B set to 1 for Byte Counter, set to 0 for Packet Counter
  T set to 1 for Sender-DSCP scoped Counter
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port2 direct measurement .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B|T| DSCP | Block Number| DSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ (4 octets) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ses-Sender TTL| MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Reflector Direct Measurement Test Packet

## Slide 5: Direct Measurement TLV vs. Direct Measurement Test Packet
 | Direct Measurement TLV | Direct Measurement Test Packet
Need TLV processing for each received packet on Session-Reflector in hardware | Yes | No
Need to write timestamp (clock sync needed for one-way delay) | Yes | N/A
Minimum bytes to load in write-able memory | 114 (Eth 18, IPv6 40, UDP 8, STAMP 44, TLV Type 4, Total = 114 Byte) | 70 (Eth 18, IPv6 40, UDP 8, Seq 4, Total = 70 Byte)
Counters at fixed location in the test packet for in-band hardware counter-stamping | No (TLV-based) | Yes
Reply test packets with counters at the fixed location for in-band hardware counter-stamping | No | Yes
Byte counters | No | Yes
64-bit packet and byte counters | No | Yes
Alternate-marking method packet loss - using block number for counters (out-of-order data packet support) | No | Yes
Per Traffic Class Counters | No | Yes

## Slide 6
Link Loss Direct Measurement (P2P Circuits)
- In-band Counter-stamping in Hardware
TX Packet Loss %
  = 100* ( ( ( C1(t) – C1(t-1) ) – ( C2(t) – C2(t-1) ) / ( C1(t) – C1(t-1) )
  = 100* ( ( (103 – 100) – (203 – 200) ) / (103 – 100) )
  = 0
Counter 1
2
1
Counter 2
HW
HW
Sender
Reflector
Advertise extended TE metrics – link loss percentage
  RFC 8570 (IS-IS)
  RFC 7471 (OSPF)
  RFC 8571 (BGP-LS)
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|A| RESERVED | Link Loss |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
110th IETF Online
6

## Slide 7: Alternate Marking Method for Packet Loss
RFC 8321 - Alternate-Marking Method for Passive and Hybrid Performance Monitoring
RFC 8957 - Synonymous Flow Label Framework
Control plane-based packet loss measurement with distributed forwarding LCs, using block number of the counters
A: packet with A coloring
B: packet with B coloring
| | | | |
| | Traffic Flow | |
------------------------------------------------------------------->
BBBBBBB AAAAAAAAAAA BBBBBBBBBBB AAAAAAAAAAA BBBBBBBBBBB AAAAAAA
------------------------------------------------------------------->
... | Block 5 | Block 4 | Block 3 | Block 2 | Block 1
| | | | |
Figure 2: Traffic Coloring

## Slide 8: Data Packet Loss Calculation
Using the Counters C1, C2, C3 and C4 as per reference topology, from the nth and (n-1)th direct measurement test packets.
  Transmit Loss TxL[n-1, n] = (C1[n] - C1[n-1]) - (C2[n] - C2[n-1])
  Receive Loss RxL[n-1, n] = (C3[n] - C3[n-1]) - (C4[n] - C4[n-1])
When using Alternate-Marking Method, all Counters used for the loss calculation belongs to the same Block Number, as described in Section 3.1 of [RFC8321].
C1 C2
/ \
+-------+ DM Test Packet +-------+
| | - - - - - - - - - - ->| |
| R1 |=======================| R3 |
| |<- - - - - - - - - - - | |
+-------+ DM Reply Test Packet +-------+
\ /
C4 C3
Session-Sender Session-Reflector
Reference Topology

## Slide 9: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 10
Thank you

## Slide 11: STAMP Test Packet with Direct Measurement TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| |
| |
+ +
| MBZ (30 octets) |
+ +
| |
| |
+ +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Sender Test Packet Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ses-Sender TTL | MBZ2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Session-Reflector Test Packet Format
110th IETF Online
11