## Slide 1: MPLS Data Plane Encapsulation for In-situ OAM Data
draft-gandhi-mpls-ioam-sr-05
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Zafar Ali - Cisco Systems (zali@cisco.com)
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Frank Brockners - Cisco Systems (fbrockne@cisco.com)
Bin Wen - Comcast (Bin_Wen@cable.comcast.com)
Voitek Kozak - Comcast (Voitek_Kozak@comcast.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Transport In-situ OAM (IOAM) data fields with MPLS Encapsulation
  Scope:
  Using data fields defined in:
    draft-ietf-ippm-ioam-data
    draft-ietf-ippm-ioam-direct-export
    draft-ietf-ippm-ioam-flags
  Edge-to-edge (E2E) IOAM
  Hop-by-hop (HbH) IOAM

## Slide 4: IOAM Data Field Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM Encapsulation in MPLS Header

## Slide 5: IOAM G-ACh Header
New Generic Associated Channel (G-ACh) Type (value TBA3) defined for IOAM
Protocol value 0001b allows to avoid incorrect IP header based hashing over ECMP paths
Block Number can be used to:
  Aggregate IOAM data collected in data plane, e.g. compute measurement metrics for each block of a flow
  Correlate IOAM data from different nodes

## Slide 6: IOAM Indicator Label
“IOAM Indicator Label” is used to indicate the presence of the IOAM data fields in the MPLS header after EOS.
Separate Label values are used for E2E and HbH IOAM to optimize IOAM processing on transit nodes:
  E2E Label TBA1
  HbH Label TBA2

## Slide 7: E2E IOAM Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Label (15) | TC |0| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| E2E IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: E2E IOAM Encapsulation in MPLS Header

## Slide 8: E2E Indicator Label Allocation Methods
Extension Label (15) and Label assigned by IANA with value TBA1
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating and decapsulating nodes
The label allocated by the decapsulating node
  Signaling/advertisement extensions to convey the label to all encapsulating nodes (out of scope)

## Slide 9: E2E IOAM Procedure
The encapsulating node inserts an E2E Indicator Label and one or more IOAM data field(s) in the MPLS header.
The decapsulating node "punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node for E2E IOAM also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.
  The decapsulating node processes IOAM data field(s).
  The decapsulating node forwards the data packet downstream.

## Slide 10: HbH IOAM Encapsulation in MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Label (15) | TC |0| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| HbH IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: HbH IOAM Encapsulation in MPLS Header

## Slide 11: HbH Indicator Label Allocation Methods
Extension Label (15) and Label assigned by IANA with value TBA2
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating, transit and decapsulating nodes

## Slide 12: HbH IOAM Procedure
The encapsulating node inserts a HbH Indicator Label and one or more IOAM data field(s) in the MPLS header.
The transit node processes HbH IOAM data field(s) and forwards the data packet including updated IOAM data field(s).
The decapsulating node "punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node for E2E IOAM also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.
  The decapsulating node processes IOAM data field(s).
  The decapsulating node forwards the data packet downstream.

## Slide 13: Next Steps
Welcome your comments and suggestions
Requesting MPLS WG adoption

## Slide 14
Thank you

## Slide 15
Backup

## Slide 16: Impact on Label Stack Size Imposed (MSD)
Available label stack size reduced
  Extension Label 15
  HbH IOAM Indicator SPL
May need to add entropy label due to ECMP path impact, further reducing available label stack size
  ELI
  Entropy Label
This is true for all schemes using eSPL, e.g., draft-cheng-mpls-inband-pm-encapsulation

## Slide 17: Transit Nodes Scan Deeper in MPLS Header
Transit nodes need to scan deeper into the MPLS header.
This is also true for ELI and EL today.
Note that with any indicator scheme, the node will have to look deeper into the packet to find the IOAM data that needs to be processed.

## Slide 18: Different FEC (SFL) for IOAM Packets
With a special FEC for IOAM packets and a "normal” FEC for data packets that don't carry IOAM info, it might mean that we drop the normal traffic while the iOAM traffic works.
This is indeed an issue with using SFL kind of approach. OAM reports the metrics of the LSP on which the normal traffic is not really flowing. The forwarding normal packets are not using the LSP used by the OAM, as there are two synonymous LSPs.

## Slide 19: IOAM Data After EoS
What if the LSP is carrying a PW or is DetNet?
What if it is a MS-PW?
In all these cases there is a CW immediately after EoS.
Then there is the universal fragmentation idea that is floating about that also wants to follow BoS.

## Slide 20: Example HbH IOAM Encapsulation Using SFL
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Synonymous IOAM-Label(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Synonymous IOAM-Label(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM Encapsulation Example with SR-MPLS Header

## Slide 21: IOAM Encapsulation Example with SR-MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PSID | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Label (15) | TC |0| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM Encapsulation Example with SR-MPLS Header

## Slide 22
Thank you