## Slide 1: In-band Performance Measurement Using TWAMP for Segment Routing Networks
draft-gandhi-spring-twamp-srpm-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)

## Slide 2: Agenda
Requirements and Scope
Probe Query and Response Messages
ECMP Support
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM) for SR links and end-to-end P2P/ P2MP SR Policies
    Applicable to SR-MPLS/SRv6 data planes
  No need to bootstrap PM session (e.g., to negotiate UDP port) - spirit of SR
    Stateless on egress node - spirit of SR
  One-way and two-way measurements
  Handle ECMP for SR Policies
  Scope:
  Use RFC 5357 (TWAMP) defined probe message formats
  User-configured IP/UDP path for probe messages

## Slide 4: Probe Query Messages
User defined IP/UDP path for PM probe messages for delay and loss measurements for SR links and end-to-end P2P/ P2MP SR Policies.
Payload contains RFC 5357/TWAMP defined message for Delay Measurement (DM).
User-configured UDP port1 is used for identifying DM probe packets.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Querier IPv4 or IPv6 Address .
. Destination IP Address = Responder IPv4 or IPv6 Address .
. Protocol = UDP .
. Router Alert Option Not Set .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Querier .
. Destination Port = User-configured Port for Delay Measurement.
. .
+---------------------------------------------------------------+
| Payload = Message as specified in Section 4.2.1 of RFC 5357 |
| | Payload = Message as specified in Section 4.1.2 of RFC 4656 |
. .
+---------------------------------------------------------------+
Figure 1: DM Probe Query Message for TWAMP

## Slide 5: LM Message Format for TWAMP
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Querier IPv4 or IPv6 Address .
. Destination IP Address = Responder IPv4 or IPv6 Address .
. Protocol = UDP .
. Router Alert Option Not Set .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Querier .
. Destination Port = User-configured Port for Loss Measurement .
. .
+---------------------------------------------------------------+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | Block Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Padding |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure 2A: LM Probe Query Message for TWAMP
Loss Measurement (LM) message defined with fixed offsets for transmit and receive traffic counters.
  Hardware friendly counter-stamping
LM Message format is also defined for authenticated mode.
User-configured UDP port2 is used for identifying LM probe packets.
  There is an LM TLV proposed in
  draft-mirsky-ippm-stamp-option-tlv

## Slide 6: Probes for SR-MPLS or SRv6 TE Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment List(0) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment List(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message as shown in Figure 1 for DM or Figure 2 for LM |
. .
+---------------------------------------------------------------+
Figure 3: Probe Query Message for SR-MPLS Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| SRH |
. END.OTP (DM) or END.OP (LM) with Target SRv6 SID .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message as shown in Figure 1 for DM or Figure 2 for LM |
. (Using IPv6 Addresses) .
. .
+---------------------------------------------------------------+
Figure 4: Probe Query Message for SRv6 Policy
For end-to-end performance measurement of SR Policy, the probe query messages are sent in-band with:
1) MPLS label stack for SR-MPLS Policies, Or,
2) SRv6 SRH with SID list and END.OTP (for DM) or END.OP (for LM) for target SID for SRv6 Policies.

## Slide 7: Probe Response Message
The probe response message is sent using the IP/UDP information from the probe query message.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Responder IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from Query .
. Protocol = UDP .
. Router Alert Option Not Set .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Responder .
. Destination Port = Source Port from Query .
. .
+---------------------------------------------------------------+
| TWAMP Payload for DM or LM |
. .
+---------------------------------------------------------------+

## Slide 8: ECMP Support
SR Policy can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages:
  For IPv4 and IPv6
    Different Destination Addresses in IP/UDP header (E.g. 127/8 for IPv4)
  For SR-MPLS
    Entropy label
  For SRv6
    Flow Label in SRH

## Slide 9: Applicability of STAMP
Message formats defined in draft-ietf-ippm-stamp can be used
TLVs defined in draft-mirsky-ippm-stamp-option-tlv can also be used

## Slide 10: Next Steps
Update direct Loss Measurement payload format:
  UDP checksum correction field, flags for packet vs. byte counters and 64-bit vs. 32-bit counters
  Discuss LM message format (draft-mirsky-ippm-stamp-option-tlv)
Updates for two-way measurement
  Update text on source-port usage
  Add Return Path
Elaborate on P2MP SR Policy
Can use both HMAC-SHA1 and HMAC-SHA-256 for integrity protection
Welcome your comments and suggestions

## Slide 11
Thank you