## Slide 1: MPLS Data Plane Encapsulation for In-situ OAM Data
draft-gandhi-mpls-ioam-sr-05
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Zafar Ali - Cisco Systems (zali@cisco.com)
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Frank Brockners - Cisco Systems (fbrockne@cisco.com)
Bin Wen - Comcast (Bin_Wen@cable.comcast.com)
Voitek Kozak - Comcast (Voitek_Kozak@comcast.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Transport In-situ OAM (IOAM) data fields with MPLS Encapsulation
  Scope:
  Using IOAM data fields defined in:
    draft-ietf-ippm-ioam-data
    draft-ietf-ippm-ioam-direct-export
    draft-ietf-ippm-ioam-flags
  Edge-to-edge (E2E) IOAM
  Hop-by-hop (HbH) IOAM (that includes E2E)

## Slide 4: Updates Since Version-02
Updates:
  Addressed MPLS-RT expert review comments
    Added IOAM G-ACh header
    Elaborate the IOAM procedures
  Clarified E2E and HbH Indicator Labels usage for different IOAM Option-Types
  Added multiple G-ACh / Control Word handling
  Editorial changes (e.g., cleanup SR text)
  Open Items:
    Discuss review comment on using IOAM FEC (SFL) for HbH IOAM

## Slide 5
MPLS Extensions

## Slide 6: IOAM G-ACh for IOAM Data Fields
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh (Type TBA3 | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: IOAM G-ACh for IOAM Data Fields

## Slide 7: IOAM G-ACh Header
New Generic Associated Channel (G-ACh) Type (value TBA3) defined for IOAM
Protocol value 0001b allows to avoid incorrect IP header based hashing over ECMP paths
Block Number can be used to:
  Aggregate IOAM data collected in data plane, e.g. compute measurement metrics for each block of a flow
  Correlate IOAM data from different nodes
https://www.iana.org/assignments/g-ach-parameters/g-ach-parameters.xhtml#mpls-g-ach-types

## Slide 8: IOAM Indicator Labels
“IOAM Indicator Label” is used to indicate the presence of the IOAM data fields after EOS in the MPLS Encapsulation.
Separate Indicator Labels are defined for E2E IOAM (for edge nodes) and HbH IOAM (for edge and intermediate nodes).
  The E2E IOAM Label allows to bypass IOAM processing on intermediate nodes in case of E2E IOAM.
In case of E2E IOAM, the IOAM Option-Type(s) in the data packets are processed on edge nodes only. The intermediate nodes ignore the IOAM Option-Type(s) carried by the data packets. Hence, only E2E Option-Type is carried in the IOAM data field.
In case of HbH IOAM, the IOAM Option-Type(s) in the data packets are processed on intermediate and edge nodes. Hence, both HbH and E2E Option-Types can be carried in the IOAM data field(s).

## Slide 9
E2E IOAM

## Slide 10: MPLS Encapsulation with E2E IOAM Data Fields
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| E2E IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh (Type TBA3) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: MPLS Encapsulation with E2E IOAM Data Fields

## Slide 11: E2E IOAM Indicator Label Allocation Methods
Extension Label (15) and Label assigned by IANA with value TBA1
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating and decapsulating nodes
The IOAM Label allocated by the decapsulating node
  Signaling/advertisement extensions needed to convey the label to all encapsulating nodes (out of scope)

## Slide 12: E2E IOAM Indicator Label - Comparisons
Method | Extra Label Stack Size (Note 2) | Location on Stack
eSPL Label | +2 (Note 1) | Bottom
Global Label, Signal/Advertise Label | +1 | Bottom
This is true for any mechanism that we are defining using eSPL
  SFC: https://tools.ietf.org/html/rfc8595
  E2E: draft-ietf-mpls-inband-pm-encapsulation
IOAM data packets may require Entropy label for ECMP to work around hashing issue due to G-ACh for IP packets

## Slide 13: E2E IOAM Procedure
E2E IOAM includes IOAM processing on encapsulating and decapsulating nodes. The only E2E Option-Type is carried in the IOAM data field.
The encapsulating node inserts an E2E Indicator Label and one or more IOAM data field(s) in the MPLS header.
The intermediate (intermediate) nodes do not process IOAM data.
The decapsulating node “punts the timestamped copy” of the data packet including IOAM data field(s).
  The decapsulating node processes IOAM data field(s) from the punted packet.
The decapsulating node also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS encapsulation.
  The decapsulating node forwards the data packet downstream.

## Slide 14
HbH IOAM

## Slide 15: MPLS Encapsulation with HbH IOAM Data Fields
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| HbH IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh (Type TBA3) | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: MPLS Encapsulation with HbH IOAM Data Fields

## Slide 16: HbH IOAM Indicator Label Allocation Methods
Extension Label (15) and Label assigned by IANA with value TBA2
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on encapsulating, intermediate and decapsulating nodes
The IOAM Label allocated by the intermediate and decapsulating nodes
  Signaling/advertisement extensions needed to convey the label to all encapsulating nodes (out of scope)

## Slide 17: HbH IOAM Indicator Label - Comparisons
Method | Extra Label Stack Size (Note 2) | Location on Stack | Scan Label Stack (Notes 1) | Different FIB Entry for Local Label than data packets
eSPL Label | +2 | Bottom | Yes | No
Global Label | +1 | Bottom | Yes | No
Signal/Advertise SFL like Label | +0 | Incoming Packet with Top Label | No | Yes
A intermediate node may have a limit on how many labels it can scan. However, with any indicator scheme, the node will have to look past EOS into the packet to find the IOAM data that needs to be processed
IOAM data packets may require Entropy label for ECMP to work around hashing issue due to G-ACh for IP packets

## Slide 18: HbH IOAM Procedure
HbH IOAM includes IOAM processing on encapsulating, intermediate and decapsulating nodes. Both HbH and E2E Option-Types can be carried in the IOAM data field(s).
The encapsulating node inserts a HbH Indicator Label and one or more IOAM data field(s) in the MPLS encapsulation.
The intermediate (intermediate) nodes process HbH IOAM data field(s) and forward the data packet including updated IOAM data field(s).
  The intermediate (intermediate) nodes may punt the timestamped copy of the data packet for further IOAM processing.
The decapsulating node "punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node processes IOAM data field(s) from the punted packet.
The decapsulating node also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS encapsulation.
  The decapsulating node forwards the data packet downstream.

## Slide 19
MPLS Encapsulation for IOAM Data Fields with Control Word and Another G-ACh

## Slide 20: IOAM Data Fields with Control Word and Another G-ACh
IOAM Data Fields, including IOAM G-ACh header are added in the MPLS encapsulation after the MPLS header.
The Control Word or another G-ACh MUST be added after the IOAM Data Fields in the packet.
This allows the intermediate nodes to easily access the HbH IOAM data field(s) after the MPLS header.
The decapsulating node can remove the MPLS encapsulation including the IOAM Data Fields and then process the Control Word or G-ACh following it.
IOAM HDR Length allows to locate the Control Word and G-ACh after the IOAM Data Fields.

## Slide 21: Generic PW Control Word [RFC4385] with IOAM Data Fields
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 0| Specified by PW Encapsulation [RFC4385] |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Example Generic PW Control Word with IOAM Data Fields

## Slide 22: MPLS Encap with Another G-ACh [RFC5586] with IOAM Data Fields
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM Indicator Label | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | Channel Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Example MPLS Encapsulation with Another G-ACh with IOAM Data Fields

## Slide 23
Thank you

## Slide 24
Example MPLS Encapsulations for IOAM Data Fields

## Slide 25: Example 1 - SR-MPLS Encapsulation with IOAM Data Fields
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PSID | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Label (15) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| E2E IOAM Indicator Label TBA1 | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
|0 0 0 1|Version| Reserved | IOAM G-ACh | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| Reserved | Block Number | IOAM-OPT-Type |IOAM HDR Length| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
| | O
| | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
~ Payload + Padding ~
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Example SR-MPLS Encapsulation with IOAM Data Fields

## Slide 26
Thank you