## Slide 1: Segment Routing with MPLS Data Plane Encapsulation for In-situ OAM Data
draft-gandhi-spring-ioam-sr-mpls-01
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Zafar Ali - Cisco Systems (zali@cisco.com)
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Frank Brockners - Cisco Systems (fbrockne@cisco.com)
Bin Wen - Comcast (Bin_Wen@cable.comcast.com)
Voitek Kozak - Comcast (Voitek_Kozak@comcast.com)
Sagar Soni - Cisco Systems (sagsoni@cisco.com)
Patrick Khordoc - Cisco Systems (pkhordoc@cisco.com)

## Slide 2: Agenda
Requirements and Scope
Procedures
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Transport In-situ OAM (IOAM) data fields with SR-MPLS Encapsulation
    OAM information (e.g. timestamps) carried by data traffic
  Scope:
  Using data fields defined in draft-ietf-ippm-ioam-data
  End-to-end IOAM
  Future: Hop-by-hop IOAM

## Slide 4: IOAM Data Field Encapsulation in SR-MPLS Header
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| IOAM Indicator Label | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| IOAM-Type | IOAM HDR LEN | RESERVED | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ I
! | O
! | A
~ IOAM Option and Data Space ~ M
| | |
| | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+<-+
| |
| |
| Payload + Padding (L2/L3/ESP/...) |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure 1: IOAM data encapsulation in SR-MPLS Header

## Slide 5: Procedure
The encapsulating node inserts the IOAM Indicator Label and one or more IOAM data field(s) in the MPLS header.
The decapsulating node "forwards and punts the timestamped copy" of the data packet including IOAM data field(s).
  The decapsulating node also pops the IOAM Indicator Label and the IOAM data field(s) from the MPLS header.

## Slide 6: Indicator Label Allocation Methods
Label assigned by IANA with value TBA1
  From Extended Special Purpose Labels (eSPL) range
Global Label allocated by a controller
  The controller provisions the label on both encapsulating and decapsulating nodes
Label allocated by the decapsulating node
  Signaling mechanism used to convey the label to all encapsulating nodes

## Slide 7: Implication on Hashing
The encapsulating node needs to make sure the IOAM data field(s) does not start with a well known protocol type (0x4 or 0x6 for IP)
Hashing function that uses the label values from the MPLS header may also now include the IOAM Indicator Label

## Slide 8: Next Steps
Additional details on ECMP hashing
Details on hop-by-hop IOAM
Welcome your comments and suggestions
Seeking WG adoption

## Slide 9
Thank you