## Slide 1: Enhanced Performance and Liveness Monitoring in Segment Routing Networks
draft-gandhi-spring-sr-enhanced-plm-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Navin Vaghamshi - Reliance (Navin.Vaghamshi@ril.com)
Moses Nagarajah - Telstra (Moses.Nagarajah@team.telstra.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Performance Delay and Loss Measurement & Liveness Monitoring
    End-to-end P2P/P2MP SR Policies
    Applicable to SR-MPLS/SRv6 data planes
  Scope:
  RFC 5357 (TWAMP) defined probe messages - TWAMP Light
  STAMP [draft-ietf-ippm-stamp] defined probe messages
  STAMP TLVs [draft-ietf-ippm-stamp-option-tlv]
  User-configured IP/UDP path for probe messages

## Slide 4: Liveness Monitoring of SR Policy
Liveness monitoring for SR Policy uses PM probes (TWAMP Light/STAMP delay measurement messages) in Loopback Mode
Probe messages sent using Segment List(s) of the SR Policy Candidate Paths
Probe messages are not punted on the remote/endpoint/reflector node
Liveness failure is notified when consecutive N number of probe messages are not received back at the sender
+-------+ t1 Probe +-------+
| | - - - - - - - - - - | |
| R1 |--------------------|| R5 |
| |<- - - - - - - - - - | |
+-------+ t4 Return Probe +-------+
Sender Reflector Endpoint
(Simply Forward)
Figure 1: Loopback Mode

## Slide 5: Enhanced Liveness Monitoring of SR Policy
Use the loopback mode enabled with network programming function.
  The network programming function optimizes the "operations of punt, add receive timestamp and inject the probe packet" on the reflector node.
The endpoint node adds the receive timestamp (at the fixed location locally provisioned consistently in the network) in the payload of the received TWAMP Light or STAMP probe message without punting the probe message in control-plane.
  Only add the receive timestamp if the source address in the probe message matches the local node address
+-------+ t1 Probe t2 +-------+
| | - - - - - - - - - - | |
| R1 |--------------------|| R5 |
| |<- - - - - - - - - - | |
+-------+ Return Probe +-------+
Sender Reflector Endpoint
(Timestamp,
Pop and Forward)
Figure: Loopback Mode Enabled with Network Programming

## Slide 6: SR-MPLS with Timestamp Label
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp Label (TBA1) | TC |S| TTL |
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Endpoint IPv4 or IPv6 Address .
. Destination IP Address = Sender IPv4 or IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload as defined in Section 4.2.1 of RFC 5357 |
| Payload as defined in Section 4.2 of STAMP |
. .
+---------------------------------------------------------------+
Figure 5: Probe Message Header for SR-MPLS with Timestamp Label
Timestamp Label (TBA1) allocated by IANA from Extended Special-Purpose MPLS Label Values
Used for Timestamp, Pop and Forward network programing function

## Slide 7: SRv6 with Timestamp and Forward Function
+---------------------------------------------------------------+
| SRH |
. <Segment List> .
. END.TSF with Target SID .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Endpoint IPv6 Address .
. Destination IP Address = Sender IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload as defined in Section 4.2.1 of RFC 5357 |
| Payload as defined in Section 4.2 of STAMP |
. .
+---------------------------------------------------------------+
Figure 6: Probe Message Header for SRv6 with Endpoint Function
Endpoint Function END.TSF is defined for Timestamp and Forward

## Slide 8: ECMP Support for SR Policy
SR Policy can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages:
  For IPv4 and IPv6
    Destination addresses in IP header (e.g. 127/8 for IPv4 and FFFF:7F00/104 for IPv6)
    Flow label in IPv6 header
  Used only when return path is also SR

## Slide 9: Next Steps
Welcome your comments and suggestions
Implementation exists
Requesting WG adoption

## Slide 10
Thank you

## Slide 11: Backup

## Slide 12: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Destination UDP port
Measurement Protocol / \ Measurement Protocol
Measurement Type / \ Measurement Type
Delay/Loss / \ Delay/Loss
Authentication Mode & Key / \ Authentication Mode & Key
Timestamp Format / \ Loss Measurement Mode
Delay Measurement Mode / \
Padding/Packet Size / \
Loss Measurement Mode / \
v v
+-------+ +-------+
| | | |
| R1 |------------| R5 |
| | | |
+-------+ +-------+
Sender Reflector

## Slide 13
Thank you