## Slide 1: Performance Measurement Using TWAMP Light for Segment Routing Networks
draft-gandhi-spring-twamp-srpm-09
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Updates Since IETF-106
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM)
    Links and End-to-end P2P/P2MP SR Paths
    Applicable to SR-MPLS/SRv6 data planes
  No need to negotiate UDP port to bootstrap PM session - spirit of SR
    Stateless on egress node - spirit of SR
  Handle ECMP for SR Paths
  Support stand-alone direct-mode loss measurement
  Scope:
  RFC 5357 (TWAMP Light) defined probe messages
  User-configured IP/UDP path for probe messages

## Slide 4: History of the Draft
Feb 2019
  Draft was published - draft-gandhi-spring-twamp-srpm-00
Mar 2019
  Presented draft-gandhi-spring-twamp-srpm-00 at IETF 104 Prague in SPRING WG
May 2019
  Added STAMP TLV for Return Path
July 2019
  Presented draft-gandhi-spring-twamp-srpm-01 at IETF 105 Montreal in IPPM WG
    Slide 9 Titled - Applicability of STAMP – STAMP is supported
Aug 2019
  draft-gandhi-spring-twamp-srpm-02 included stand-alone LM messages
Nov 2019
  SPRING Chairs announced in the meeting the agreement with IPPM chairs to progress the draft in SPRING WG
  Presented draft-gandhi-spring-twamp-srpm-04 at IETF 106 Singapore in SPRING WG
Mar 2020
  Moved STAMP support to draft-gandhi--spring-stamp-srpm-00
  Keep TWAMP Light support as informational in draft-gandhi-spring-twamp-srpm-08

## Slide 5: Updates Since IETF-106 (Version-04)
Updates:
  Defined Control Code for “In-band Response Requested” for TWAMP Light
    Updated Two-way mode procedure using the Control Code
  Moved STAMP support to a new draft - draft-gandhi-spring-stamp-srpm-00
  Informational draft - as TWAMP Light is informational, see Appendix I in RFC 5357 and Appendix A RFC 8545
  Various editorial changes
  Open Items:
    None

## Slide 6: TWAMP Light Control Code Field
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ |Se Control Code|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
Figure: Control Code in TWAMP Light Query Message
For a Query: Sender Control Code
0x0: Out-of-band Response Requested.
This is also the default behavior.
0x1: In-band Response Requested.
Indicates that this query has been sent over a bidirectional path and the probe response is required over the same path in the reverse direction.
The bidirectional path does not have to be an SR path.
For a Response: Reflector Control Code
0x1: Error - Invalid Message.
Indicates that the operation failed because the received query message could not be processed.
0xN: Additional Error will be defined in future
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Error Estimate | MBZ |Re Control Code|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ses-Sender TTL | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
Figure: Control Code in TWAMP Light Response Message

## Slide 7: Performance Measurement Modes
One-way Measurement Mode
  Reply sent “out of band” on IP/UDP path - default
Two-way Measurement Mode
  Reply sent “in-band” on reverse SR path
    Based on Control Code from the probe query message
Loopback Measurement Mode
  Probe message carries the return path in the header of the packet

## Slide 8: Next Steps
Welcome your comments and suggestions
Implementation exists
In WG adoption (SPRING WG) queue
Keep IPPM WG in the loop about the milestones

## Slide 9
Thank you

## Slide 10: Backup

## Slide 11: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Destination UDP port
Measurement Protocol / \ Measurement Protocol
Measurement Type / \ Measurement Type
Delay/Loss / \ Delay/Loss
Authentication Mode & Key / \ Authentication Mode & Key
Timestamp Format / \ Loss Measurement Mode
Delay Measurement Mode / \
Loss Measurement Mode / \
v v
+-------+ +-------+
| | | |
| R1 |------------| R5 |
| | | |
+-------+ +-------+
Sender Reflector

## Slide 12: Probe Query for Links
User-configured destination UDP port1 is used for DM probe messages and port2 is used for LM probe messages, both in unauthenticated mode.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv4 or IPv6 Address .
. Destination IP Address = Reflector IPv4 or IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = DM Message as specified in Section 4.2.1 of RFC 5357|
. Payload = DM Message as specified in Section 4.1.2 of RFC 5357.
. Payload = LM Message as specified in this document .
. .
+---------------------------------------------------------------+
Figure: Probe Query Message

## Slide 13: Probe Query for SR-MPLS and SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DM or LM Query Message including IP/UDP Header |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SR-MPLS Policy
For end-to-end performance delay/loss measurement of SR Policy, the probe query message is sent on the SR Policy with:
MPLS label stack for SR-MPLS Policies
SRv6 SRH [RFC 8754] with SID list for SRv6 Policies
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv6 Address .
. Destination IP Address = Next Hop IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <SID List> .
. .
+---------------------------------------------------------------+
| IP Header (Optional) |
. Source IP Address = Sender IPv6 Address .
. Destination IP Address = Reflector IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Payload = DM or LM Query Message |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SRv6 Policy

## Slide 14: Probe Response Message
The probe response message is sent using the IP/UDP information from the probe query message.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Reflector IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from Query .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Reflector .
. Destination Port = Source Port from Query .
. .
+---------------------------------------------------------------+
| Payload = DM Message specified in Section 4.2.1 of RFC 5357 | |
. Payload = LM Message specified in this document .
. .
+---------------------------------------------------------------+
Figure: Probe Response Message

## Slide 15: Stand-alone LM Message Format for TWAMP Light
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv4 or IPv6 Address .
. Destination IP Address = Reflector IPv4 or IPv6 Address .
. Protocol = UDP .
. Router Alert Option Not Set .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port2 for Loss Measurement.
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved | Block Number | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved |Sender Block Nu| MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | Padding (3 Bytes) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Padding |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Loss Measurement (LM) message defined
  Hardware efficient counter-stamping
    Well-known locations for transmit and receive traffic counters
  Stand-alone LM message, not tied to DM
LM message format is also defined for authenticated mode
User-configured destination UDP port2 is used for identifying LM probe packets
Does not modify existing TWAMP Light (which is for DM) procedure as different UDP destination port2 is used for LM

## Slide 16: ECMP Support for SR Path
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8)
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 17
Thank you