## Slide 1: Enhanced Performance Delay and Liveness Monitoring in Segment Routing Networks
draft-gandhi-spring-sr-enhanced-plm-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Navin Vaghamshi - Reliance (Navin.Vaghamshi@ril.com)
Moses Nagarajah - Telstra (Moses.Nagarajah@team.telstra.com)
Richard Foote - Nokia (footer.foote@nokia.com)

## Slide 2: Agenda
Requirements and Scope
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Performance Delay Monitoring & Liveness Monitoring in SR networks
    End-to-end P2P/P2MP SR paths
    Applicable to SR-MPLS/SRv6 data planes
  Running single protocol in SR networks
    Simplify implementations and reduce development cost
    Simplify deployment and reduce operational complexity
  No reflector dependency
    Stateless on reflector (e.g. reflector unaware of the monitoring protocol)
      State is in the probe message - spirit of SR
    Higher scale and faster detection interval
  Scope:
  RFC 5357 (TWAMP Light) defined probe messages
  RFC 8762 (Simple TWAMP (STAMP)) defined probe messages

## Slide 4: History of the Draft
March 2020
  Draft was published
April 2020
  Presented version 00 in IETF 107 Virtual MPLS WG Meeting
July 2020
  Presented version 02 in IETF 108 Online SPRING WG meeting

## Slide 5: PM Probes in Loopback Mode for SR Policy
Using PM probes (TWAMP Light/Simple TWAMP (STAMP) delay measurement messages) in Loopback Mode
Probe messages sent using Segment List(s) of the SR Policy Candidate Path(s)
Probe messages are not punted on the reflector node out of fast-path in forwarding
Reflector is agnostic of the monitoring protocol
t1
/
+-------+ Probe +-------+
| | - - - - - - - - - - | |
| R1 |====================|| R5 |
| |<- - - - - - - - - - | |
+-------+ Return Probe +-------+
\
t4
Sender Reflector
(Forward, Not Punt)
Figure: PM Loopback Mode

## Slide 6: Enhanced Performance Delay and Liveness Monitoring of SR Policy
Using PM probes in loopback mode enabled with network programming function
  The network programming function optimizes the "operations of punt and inject the probe packet" on the reflector node
  As probe packets are forwarded in fast-path, faster liveness failure detection is possible
Reflector node adds the receive timestamp in the payload of the received probe message in the fast-path
  Only adds the receive timestamp if the source address or destination address in the probe message matches the local node address
  Ensure loopback probe packets return from the intended reflector node
t1 t2
/ \ +-------+ Probe +-------+
| | - - - - - - - - - - | |
| R1 |====================|| R5 |
| |<- - - - - - - - - - | |
+-------+ Return Probe +-------+
Sender Reflector
(Timestamp,
Pop and Forward)
Figure: Loopback Mode Enabled with Network Programming

## Slide 7: Notifications
Delay metrics are notified when consecutive M number of probe messages have delay values exceed the configured thresholds
Liveness failure (bring-down - loss of heart beats) is notified when consecutive N number of return probe messages are not received at the sender
Liveness success (bring-up - success of heart beats) is notified as soon as one or more return probe messages are received at the sender

## Slide 8: Probe Messages for Timestamp and Forward Function
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp (t1) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp (t2) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | |
+-+-+-+-+-+-+-+-+ |
| |
~ Padding ~
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: TWAMP Light Probe Message Format
Leverage existing TWAMP implementations and deployments
Sender adds Transmit Timestamp (t1)
Reflector adds Receive Timestamp (t2) at fixed offset in payload locally provisioned (consistently in the network)
  E.g. offset-byte 16 from the start of the TWAMP payload
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Timestamp (t1) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp (t2) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: STAMP Probe Message Format

## Slide 9: SR-MPLS with Timestamp and Forward Function
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Label(1) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ . . . . . . +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Label(n) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Extension Label (15) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Timestamp Label (TBA1) | TC |S| TTL | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | IP Header | . Source IP Address = Reflector IPv4 or IPv6 Address . . Destination IP Address = Sender IPv4 or IPv6 Address .
. .
+---------------------------------------------------------------+ | UDP Header | . Source Port = As chosen by Sender . . Destination Port = As chosen by Sender . . . +---------------------------------------------------------------+ | Payload |
. . +---------------------------------------------------------------+
Example Probe Message with Timestamp Label for SR-MPLS
Extended Special-purpose label (TBA1) is defined for Timestamp and Forward network programming
Reverse Path can be IP or SR-MPLS
Source and Destination Addresses are swapped that represent the Reverse direction path

## Slide 10: SRv6 with Timestamp and Forward SID Function
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. End.TSF with Reflector SID .
. .
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Reflector IPv6 Address .
. Destination IP Address = Sender IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = As chosen by Sender .
. .
+---------------------------------------------------------------+
| Payload |
. .
+---------------------------------------------------------------+
Example Probe Message with Endpoint Function for SRv6
Endpoint SID Function End.TSF is defined for Timestamp and Forward network programming and is carried for the Reflector node SID
Reverse path can be IP
  Reflector node removes SRH
Reverse path can be SR
  Reverse direction SR path Segment-list carried in SRH
  Reflector node does not remove the SRH
Source and Destination Addresses are swapped that represent the Reverse direction path in the inner IPv6 header

## Slide 11: ECMP Support for SR Paths
SR Paths can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
PM probe messages can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages. Examples are:
  For IPv4 when return path is also SR-MPLS
    Sweeping destination address in IPv4 header (e.g. 127/8)
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 12: Example Provisioning Model
+------------+
| Controller |
+------------+
PDLM Mode / \ Network Programming Label
LB or Enhanced Mode / \ Timestamp2 Offset
Measurement Protocol / \ Timestamp Format
Missed Probe Message Count / \
Network Programming Label / \
Timestamp Format / \
Delay threshold/Count / \
Source/Dest UDP Ports / \
v v
+-------+ +-------+
| | | |
| R1 |============| R5 |
| | SR Path | |
+-------+ +-------+
Sender Reflector
Figure 2: Example Provisioning Model

## Slide 13: Next Steps
Welcome your comments and suggestions
Requesting SPRING WG adoption

## Slide 14
Thank you

## Slide 15: Backup

## Slide 16: Loopback Mode with Timestamp and Forward for SR-MPLS Policy
Probe
Return Probe
2 PE
3
4 PE
24134
15
TS LABEL TBA1
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1
15
TS LABEL TBA1
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1, Timestamp2
IPv4/UDP Source: PE4 Destination: PE2
Payload Timestamp1, Timestamp2

## Slide 17
Thank you