## Slide 1: Performance Measurement for Segment Routing Networks with MPLS Data Plane
draft-gandhi-mpls-rfc6374-sr-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Stefano Salsano - Universita di Roma "Tor Vergata" (stefano.salsano@uniroma2.it)
Mach Chen - Huawei (mach.chen@huawei.com)
Sagar Soni - Cisco Systems (sagsoni@cisco.com)
Zafar Ali - Cisco Systems (zali@cisco.com)
Pier Luigi Ventre - CNIT (pierluigi.ventre@cnit.it)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Updates Since IETF-106
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM)
    SR Links and end-to-end P2P/ P2MP SR Policies
  Delay and Loss extended TE link metrics advertisement in the network
  One-way, two-way and loopback measurement modes
  Scope:
    Segment Routing (SR) with MPLS data plane
    RFC 6374 for probe query and response messages
    RFC 7876 (UDP return path) for probe response messages

## Slide 4: History of the Draft
Feb 14, 2018
  Draft was first published draft-gandhi-spring-sr-mpls-pm
July 2018
  Draft was introduced at IETF 102 Montreal in SPRING WG
Nov 2018
  Presented revision-03 draft-gandhi-spring-sr-mpls-pm of at IETF 103 Bangkok in SPRING and IPPM WGs
Feb 14, 2019
  Draft was renamed to draft-gandhi-spring-rfc6374-srpm-mpls
Mar 2019
  Presented revision-00 of draft-gandhi-spring-rfc6374-srpm-mpls at IETF 104 Prague in SPRING WG
Oct 2019
  Chairs agreed to progress the work in MPLS WG
  Draft renamed to draft-gandhi-mpls-rfc6374-sr
Nov 2019
  Presented revision-00 of draft-gandhi-mpls-rfc6374-sr in MPLS WG

## Slide 5: Updates Since IETF-106
Updates:
  Updated procedure for Two-way measurement mode
  Identify the Return Path TLV and Block Number TLV as mandatory TLVs
  Added Destination Address TLV handling
  Addressed various review comments
  Various editorial changes
Open Items:
    None

## Slide 6: Measurement Modes for SR Policy
One-way Measurement Mode
  Reply sent out of band IP/UDP path using RFC 7876 mechanisms
Two-way Measurement Mode
  Reply sent in-band using the RFC 6374 mechanisms (using Control code)
  Return Path TLV can be used from the probe query message for SR Policies
Loopback Measurement Mode
  Probe message carries the return path label stack in the header of the packet

## Slide 7: Return Path TLV for Two-way Measurement
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = TBA1 | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Return Path Sub-TLVs |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Return Path TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(1) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(n) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Segment List Sub-TLV in Return Path TLV
Sub-TLVs
Type (value 1): SR-MPLS Segment List (Label Stack) of the Reverse SR Path
Type (value 2): SR-MPLS Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
TLV is mandatory when used and if responder does not support, it MUST return Error 0x17: Unsupported Mandatory TLV Object

## Slide 8: Block Number TLV for Loss Measurement
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type TBA2 | Length | Reserved | Block Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Block Number TLV
Carry the Block Number (8-bit) of the traffic counters in the probe query and response messages for loss measurement
When using Alternate Marking Method to identify and correlate the counters from the two end-points
TLV is mandatory when used and if responder does not support, it MUST return Error 0x17: Unsupported Mandatory TLV Object

## Slide 9: Destination Address TLV (Type 129) Handling
To ensure that the probe query message is processed by the intended responder node, Destination Address TLV [RFC6374] can be sent in the probe query message.
The responder node only replies with Success in Control Code if it is the intended destination for the probe query.
Otherwise, it MUST return 0x15: Error - Invalid Destination Node Identifier.

## Slide 10: Next Steps
Welcome your comments and suggestions
Has been implemented
Requested WG adoption in MPLS WG

## Slide 11
Thank you

## Slide 12: PM Probes for SR Links
For SR links, the PM probe query messages for link delay and packet loss measurements are sent using MPLS GAL/GAch header as defined in [RFC6374].
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| GAL (value 13) | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 1|Version| Reserved | GAL Channel Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Probe Packet Header for an SR-MPLS Link

## Slide 13: SR Link Extended TE Metrics Advertisement
Measure delay and loss performance of SR Links.
Compute SR Link Delay metrics (minimum-delay, maximum-delay, average-delay, delay-variance) and SR Link Packet Loss metric.
SR link extended TE metrics advertised in the network using the TLVs defined in the following RFCs/Drafts:
  OSPF [RFC7471]
  ISIS [RFC7810] [RFC8570]
  BGP-LS [RFC8571]

## Slide 14: PM Probes for SR Policy
For end-to-end measurement of SR Policy, the PM probe query messages for delay and loss measurements are sent on the congruent path with data traffic using MPLS GAL/GAch header as defined in [RFC6374] and SR-MPLS label stack of the SR Policy.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Label(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PSID | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| GAL (value 13) | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 1|Version| Reserved | GAL Channel Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Probe Packet Header for an End-to-end SR-MPLS Policy

## Slide 15: PM Probes for P2MP SR Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Replication SID | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| GAL (value 13) | TC |1| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0 0 1|Version| Reserved | GAL Channel Type |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: P2MP SR-MPLS Policy
The sender root node sends probe query messages using the Replication Segment for the P2MP SR Policy
Each responder leaf node adds the "Source Address" TLV (Type 130) [RFC6374] with its IP address in the probe response messages.
  This TLV allows the sender root node to identify the responder leaf nodes of the P2MP SR Policy

## Slide 16: WG Co-ordination Plan
IANA code-points allocated by MPLS WG
Keep SPRING WG in the loop for SR aspects
  Post draft updates to SPRING mailing list as well
  Inform SPRING WG about the milestones (adoption, Last Call)
From Bruno:
  Please keep SPRING in the loop for the SPRING specific content