## Slide 1: Simple TWAMP (STAMP) Extensions for Segment Routing Networks
draft-gandhi-ippm-stamp-srpm-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM)
    Links and End-to-end P2P/P2MP SR Paths
    Applicable to SR-MPLS/SRv6 data planes
  Support stand-alone direct-mode loss measurement
  Scope:
  STAMP [RFC 8762]
  STAMP TLVs [draft-ietf-ippm-stamp-option-tlv]

## Slide 4: History of the Draft
Feb 2019
  Draft was published - draft-gandhi-spring-twamp-srpm-00
Mar 2019
  Presented draft-gandhi-spring-twamp-srpm-00 at IETF 104 Prague in SPRING WG
May 2019
  Added STAMP TLV for Return Path
July 2019
  Presented draft-gandhi-spring-twamp-srpm-01 at IETF 105 Montreal in IPPM WG
    Slide 9 Titled - Applicability of STAMP
Nov 2019
  SPRING Chairs announced in the meeting the agreement with IPPM chairs to progress the draft in SPRING WG
  Presented draft-gandhi-spring-twamp-srpm-04 at IETF 106 Singapore in SPRING WG
Mar 2020
  Moved STAMP support to draft-gandhi-spring-stamp-srpm-00
  Keep TWAMP Light support as informational in draft-gandhi-spring-twamp-srpm-08
Jul 2020
  Presented draft-gandhi-spring-stamp-srpm-01 at IETF 108 in SPRING and IPPM WG
October 2020
  Split draft into draft-gandhi-spring-stamp-srpm-03 and draft-gandhi-ippm-stamp-srpm-00

## Slide 5: STAMP Control Code Field
In a Query: Sender Control Code
0x0: Out-of-band Response Requested.
This is also the default (current) behavior.
0x1: In-band Response Requested.
Indicates that this query has been sent over a bidirectional path and the probe response is required over the same path in reverse direction.
0x2: No Response Requested.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Sequence Number | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Timestamp | | | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ |Se Control Code|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| MBZ (24 octets) |
| |
| |
| |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Sender Control Code in STAMP DM Message
With this, the reflector node does not require any additional SR state for PM (recall that in SR networks, the state is in the probe packet and signaling of the parameters is avoided).
Also applicable to non-SR paths.

## Slide 6: Destination Address in STAMP Node Address TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Address Family |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Address ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Node Address TLV Format
Destination Node Address (value TBA1):
Indicates the address of the intended recipient node of the query message.
The reflector node MUST NOT send response if it is not the intended destination node of the query.
Useful when query is sent with 127/8 destination address.

## Slide 7: Return Address in STAMP Return Path TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type = TBA2 | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Return Path Sub-TLVs |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Return Path TLV
Return Path (value TBA2):
Sub-TLVs Types:
Type (value 1): Return Address. Target node address of the response; different than the Source Address in the query
Type (value 2): SR-MPLS Label Stack of the Reverse SR Path
Type (value 3): SR-MPLS Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
Type (value 4): SRv6 Segment List of the Reverse SR Path
Type (value 5): SRv6 Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Segment List Sub-TLV in Return Path TLV

## Slide 8: Stand-alone Direct-mode LM Message Format for STAMP
Stand-alone Direct-mode Loss Measurement (LM) message defined
  Hardware efficient counter-stamping
    Well-known locations for transmit and receive traffic counters
  Stand-alone LM message, not tied to DM
Direct-mode LM message format is also defined for authenticated mode
User-configured destination UDP Port2 is used for identifying LM probe packets
Does not modify existing STAMP (which is for DM) procedure as different destination UDP is used for LM
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv4 or IPv6 Address .
. Destination IP Address = Reflector IPv4 or IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port2 for Loss Measurement.
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved | Block Number | SSID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved |Sender Block Nu| MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 9: Next Steps
Welcome your comments and suggestions
Implementation exists
Request IPPM WG adoption

## Slide 10
Thank you