## Slide 1: Performance Measurement Using TWAMP Light for Segment Routing Networks
draft-gandhi-spring-twamp-srpm-11
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Summary of Procedures
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM)
    Links and End-to-end P2P/P2MP SR Paths
      Links include physical, virtual, LAG (bundle), LAG member, numbered/unnumbered links
    Applicable to SR-MPLS/SRv6 data planes
  No need to signal to PM parameters - spirit of SR
    Stateless on egress node - spirit of SR
    State is in the probe message
  Handle ECMP for SR Paths
  Support stand-alone direct-mode loss measurement
  Scope:
  RFC 5357 (TWAMP Light) defined probe messages
  User-configured IP/UDP path for probe messages

## Slide 4: History of the Draft
Feb 2019
  Draft was published - draft-gandhi-spring-twamp-srpm-00
Mar 2019
  Presented draft-gandhi-spring-twamp-srpm-00 at IETF 104 Prague in SPRING WG
July 2019
  Presented draft-gandhi-spring-twamp-srpm-01 at IETF 105 Montreal in IPPM WG
    Slide 9 Titled - Applicability of STAMP
Nov 2019
  SPRING Chairs announced in the meeting the agreement with IPPM chairs to progress the draft in SPRING WG
  Presented draft-gandhi-spring-twamp-srpm-04 at IETF 106 Singapore in SPRING WG
Mar 2020
  Moved STAMP support to draft-gandhi-spring-stamp-srpm-00
  Keep TWAMP Light support as informational in draft-gandhi-spring-twamp-srpm-08
Jul 2020
  Presented draft-gandhi-spring-twamp-srpm-09 at IETF 109 in IPPM WG
October 2020
  Split draft into draft-gandhi-spring-twamp-srpm-11 and draft-gandhi-ippm-twamp-srpm-00

## Slide 5: TWAMP Light - Summary of PM Drafts
draft-gandhi-spring-twamp-srpm
Defines procedures for delay, synthetic loss and direct-mode loss measurements
  For Links and end-to-end SR Paths for SR-MPLS and SRv6 data planes
draft-gandhi-ippm-twamp-srpm
Defines extensions for TWAMP Light for Segment Routing
  Defines Session-Sender Control Code field for in-band response request
  Defines stand-alone direct-mode loss measurement query and response messages

## Slide 6: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Destination UDP port
Measurement Protocol / \ Measurement Protocol
Measurement Type / \ Measurement Type
Delay/Loss / \ Delay/Loss
Authentication Mode & Key / \ Authentication Mode & Key
Timestamp Format / \ Loss Measurement Mode
Delay Measurement Mode / \
Loss Measurement Mode / \
v v
+-------+ +-------+
| | | |
| R1 |============| R5 |
| | SR Path | |
+-------+ Or Link +-------+
Session-Sender Session-Reflector

## Slide 7: Probe Query for Links
User-configured destination UDP port1 is used for DM probe messages and port2 is used for direct-mode LM probe messages (unauthenticated mode)
Applicable to physical, virtual, LAG, LAG member, numbered/unnumbered links – probe messages pre-routed over the links
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv4 or IPv6 Address .
. Destination IP Address = Session-Reflector IPv4 or IPv6 Addr .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = DM Message as specified in Section 4.2.1 of RFC 5357|
. Payload = DM Message as specified in Section 4.1.2 of RFC 5357.
. Payload = LM Message as specified in this document .
. .
+---------------------------------------------------------------+
Figure: Probe Query Message

## Slide 8: Probe Query for SR-MPLS and SRv6 Policy
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| DM or LM Query Message including IP/UDP Header |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SR-MPLS Policy
For performance delay/loss measurement of end-to-end SR Policy, the probe query message is sent on the SR Policy with:
MPLS label stack of SR-MPLS Policy
SRv6 SRH [RFC 8754] with Segment List of SRv6 Policy
Same user-configured destination UDP port1 is used for DM probe messages and port2 is used for direct-mode LM probe messages (unauthenticated mode) – same as Links.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Destination IPv6 Address .
. .
+---------------------------------------------------------------+
| SRH as specified in RFC 8754 |
. <Segment List> .
. .
+---------------------------------------------------------------+
| IP Header (as needed) |
. Source IP Address = Session-Sender IPv6 Address .
. Destination IP Address = Session-Reflector IPv6 Address .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = DM or LM Query Message |
. .
+---------------------------------------------------------------+
Figure: Example Probe Query Message for SRv6 Policy

## Slide 9: Probe Response Message
The probe response message is sent using the IP/UDP information from the probe query message.
Based on Control Code from the probe query message
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Session-Reflector IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from Query .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Session-Reflector .
. Destination Port = Source Port from Query .
. .
+---------------------------------------------------------------+
| Payload = DM Message specified in Section 4.2.1 of RFC 5357 or|
. Payload = LM Message specified in this document .
. .
+---------------------------------------------------------------+
Figure: Probe Response Message

## Slide 10: ECMP Support for SR Path
SR Path can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to probe messages. Examples are:
  For IPv4
    Sweeping destination address in IPv4 header (e.g. 127/8)
  For IPv6
    Sweeping flow label in IPv6 header

## Slide 11: Performance Measurement Modes
One-way Measurement Mode
  Reply sent “out of band” on IP/UDP path - default
Two-way Measurement Mode
  Reply sent “in-band” on reverse SR path
    Based on Control Code from the probe query message
Loopback Measurement Mode
  Probe message carries the return path in the header of the packet

## Slide 12: Example PM Metrics
PM probe packets can be used to compute following delay metrics:
  Minimum delay
  Maximum delay
  Average delay
  Delay variance
PM probe packet loss can be used to compute following loss metrics:
  Synthetic packet loss (aka indirect-mode packet loss measurement)
  Connection loss (aka liveness heart-beat failure)

## Slide 13: Next Steps
Welcome your comments and suggestions
Request SPRING WG adoption

## Slide 14
Thank you