## Slide 1: Performance Measurement Using STAMP for Segment Routing Networks
draft-gandhi-spring-stamp-srpm-00
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
History of the Draft
Updates Since IETF-106
Summary
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Delay and Loss Performance Measurement (PM)
    Links and End-to-end P2P/P2MP SR Policies
    Applicable to SR-MPLS/SRv6 data planes
  No need to bootstrap PM session (e.g. to negotiate UDP port) - spirit of SR
    Stateless on egress node - spirit of SR
  Handle ECMP for SR Policies
  Support stand-alone direct-mode loss measurement
  Scope:
  STAMP [RFC 8762]
  STAMP TLVs [draft-ietf-ippm-stamp-option-tlv]

## Slide 4: History of the Draft
Feb 2019
  Draft was published - draft-gandhi-spring-twamp-srpm-00
May 2019
  Added STAMP TLV for Return Path
Mar 2019
  Presented revision-00 at IETF 104 Prague in SPRING WG
July 2019
  Presented revision-01 at IETF 105 Montreal in IPPM WG
    Slide 9 Titled - Applicability of STAMP – STAMP is supported
Aug 2019
  Revision-02 updates included a section on stand-alone LM messages
Nov 2019
  SPRING Chairs announced in the meeting the agreement with IPPM chairs to progress the draft in SPRING WG
  Presented revision-04 at IETF 106 Singapore in SPRING WG
Mar 2020
  Moved STAMP support to draft-gandhi--spring-stamp-srpm-00
  Scope TWAMP Light support as informational in draft-gandhi-spring-twamp-srpm-08

## Slide 5: Updates Since IETF-106 (Revision-04)
Updates:
  Defined Control Code for “In-band Response Requested” for STAMP
    Updated Two-way mode procedure using the Control Code
  Defined Destination Address in STAMP Node Address TLV to identify the intended Destination node
  Added Return Address Sub-TLV in the STAMP Return Path TLV to send response to a specific node
  Various editorial changes
  Open Items:
    Identify TLV as Mandatory or Optional
    Update IANA registry action

## Slide 6: STAMP Control Code Field
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | Session ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| MBZ |Se Control Code|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Error Estimate | MBZ |Re Control Code|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ses-Sender TTL | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
Figure 6: Sender and Reflector Control Code in STAMP DM Message
For a Query: Sender Control Code
0x0: Out-of-band Response Requested.
This is also the default behavior.
0x1: In-band Response Requested.
Indicates that this query has been sent over a bidirectional path and the probe response is required over the same path in reverse direction.
The bidirectional path does not have to be an SR path.
For a Response: Reflector Control Code
0x1: Error - Invalid Message.
Indicates that the operation failed because the received query message could not be processed.
0xN: Additional Error will be defined in future.

## Slide 7: Performance Measurement Modes
One-way Measurement Mode
  Reply sent “out of band” on IP/UDP path by default
Two-way Measurement Mode
  Reply sent “in-band” on reverse SR path
    Based on Control Code from the probe query message
  Use Return Path TLV for STAMP from the probe query message
Loopback Measurement Mode
  Probe message carries the return path in the header of the packet

## Slide 8: Destination Address in STAMP Node Address TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Address Family |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Address ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Node Address TLV Format
Destination Node Address (value TBA1):
Indicates the address of the intended recipient node of the query message.
The reflector node SHOULD NOT send response if it is not the intended destination node of the query.
Useful when query is sent with 127/8 destination address.

## Slide 9: Return Address in STAMP Return Path TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = TBA2 | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Return Path Sub-TLVs |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Return Path TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Segment List Sub-TLV in Return Path TLV
Return Path (value TBA2):
Sub-TLVs:
Type (value 0): Return Address. Target node address of the response different than the Source Address in the query
Type (value 1): SR-MPLS Label Stack of the Reverse SR Path
Type (value 2): SR-MPLS Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy
Type (value 3): SRv6 Segment List of the Reverse SR Path
Type (value 4): SRv6 Binding SID [draft-ietf-pce-binding-label-sid] of the Reverse SR Policy

## Slide 10: Stand-alone LM Message Format for STAMP
Loss Measurement (LM) message defined
  Hardware efficient counter-stamping
    Well-known locations for transmit and receive traffic counters
  Stand-alone LM message, not tied to DM
LM message format is also defined for authenticated mode
User-configured destination UDP Port2 is used for identifying LM probe packets
Does not modify existing STAMP (which is for DM) procedure as different UDP destination Port2 is used for LM.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv4 or IPv6 Address .
. Destination IP Address = Reflector IPv4 or IPv6 Address .
. Protocol = UDP .
. Router Alert Option Not Set .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port2 for Loss Measurement.
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transmit Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved | Block Number | Session ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender Counter |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|X|B| Reserved |Sender Block Nu| MBZ |Re Control Code|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sender TTL | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 11: Next Steps
Welcome your comments and suggestions
Implementation exists
In WG adoption (SPRING WG) queue
Keep IPPM WG in the loop about the milestones

## Slide 12
Thank you

## Slide 13: Backup

## Slide 14: Example Provisioning Model
+------------+
| Controller |
+------------+
Destination UDP Port / \ Destination UDP port
Measurement Protocol / \ Measurement Protocol
Measurement Type / \ Measurement Type
Delay/Loss / \ Delay/Loss
Authentication Mode & Key / \ Authentication Mode & Key
Timestamp Format / \ Loss Measurement Mode
Delay Measurement Mode / \
Loss Measurement Mode / \
v v
+-------+ +-------+
| | | |
| R1 |------------| R5 |
| | | |
+-------+ +-------+
Sender Reflector

## Slide 15: Probe Query for Links
User-configured destination UDP port1 is used for DM probe messages in unauthenticated mode and port2 is used for LM probe messages in unauthenticated mode.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Sender IPv4 or IPv6 Address .
. Destination IP Address = Reflector IPv4 or IPv6 Address .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Sender .
. Destination Port = User-configured Port .
. .
+---------------------------------------------------------------+
| Payload = DM Message | |
. Payload = LM Message .
. .
+---------------------------------------------------------------+
Figure: Probe Query Message

## Slide 16: Probe Query for SR-MPLS and SRv6 Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) | TC |S| TTL |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message for DM or LM |
. .
+---------------------------------------------------------------+
Figure: Probe Query Message for SR-MPLS Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| SRH |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Message for DM or LM |
. (Using IPv6 Addresses) .
. .
+---------------------------------------------------------------+
Figure: Probe Query Message for SRv6 Policy
For end-to-end performance delay/loss measurement of SR Policy, the probe query messages are sent on the SR Policy path with:
MPLS label stack for SR-MPLS Policies
SRv6 SRH [RFC 8754] with SID list for SRv6 Policies

## Slide 17: Probe Response Message
The probe response message is sent using the IP/UDP information from the probe query message.
+---------------------------------------------------------------+
| IP Header |
. Source IP Address = Reflector IPv4 or IPv6 Address .
. Destination IP Address = Source IP Address from Query .
. Protocol = UDP .
. .
+---------------------------------------------------------------+
| UDP Header |
. Source Port = As chosen by Reflector .
. Destination Port = Source Port from Query .
. .
+---------------------------------------------------------------+
| DM Payload | |
. LM Payload .
. .
+---------------------------------------------------------------+
Figure: Probe Response Message

## Slide 18: ECMP Support for SR Policy
SR Policy can have ECMP between the ingress and transit nodes, between transit nodes and between transit and egress nodes.
Sending PM probe queries that can take advantage of the hashing function in forwarding plane.
Existing forwarding mechanisms are applicable to PM probe messages:
  For IPv4 and IPv6
    Destination addresses in IP header (e.g. 127/8 for IPv4 and FFFF:7F00/104 for IPv6)
    Flow label in IPv6 header

## Slide 19: Backup

## Slide 20: STAMP DM Message with Direct Measurement TLV (DM+LM Combined Probe Message)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| |
| |
+ +
| MBZ (30 octets) |
+ +
| |
| |
+ +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Direct Measurement Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Sender Message Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Receive Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Error Estimate | MBZ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Ses-Sender TTL | MBZ2 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Direct Measurement Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Sender Tx counter (S_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Rx counter (R_RxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Session-Reflector Tx counter (R_TxC) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Reflector Message Format
IETF IPPM Interim – April 2020
20

## Slide 21
Thank you