## Slide 1: Simple TWAMP (STAMP) Extensions for Segment Routing Networks
draft-gandhi-ippm-stamp-srpm-02
Rakesh Gandhi - Cisco Systems (rgandhi@cisco.com) - Presenter
Clarence Filsfils - Cisco Systems (cfilsfil@cisco.com)
Daniel Voyer - Bell Canada (daniel.voyer@bell.ca)
Mach(Guoyi) Chen - Huawei (mach.chen@huawei.com)
Bart Janssens - Colt (Bart.Janssens@colt.net)

## Slide 2: Agenda
Requirements and Scope
Summary of Extensions
Next Steps

## Slide 3: Requirements and Scope
Requirements:
  Support in-band Performance Measurement for links and SR paths
Goals:
  Avoid provisioning test sessions on Session-Reflector for stateless mode
  Avoid control protocol for signaling dynamic parameters
  High scale for number of test sessions and faster detection interval
    Support hardware implementation
  Scope:
  STAMP [RFC 8762]
  STAMP Extensions [RFC 8972]

## Slide 4: STAMP Destination Node Address TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type = TBA1 | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Address Family |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Address ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Destination Node Address TLV Format
Destination Node Address TLV (value TBA1):
Indicates the address of the intended destination of the Session-Sender test packet.
The Session-Reflector that supports this TLV, MUST NOT send reply if it is not the intended destination of the Session-Sender test packet.
Useful when test packet is sent with 127/8 destination address (e.g. sweeping ECMP paths).

## Slide 5: STAMP Return Path TLV
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type = TBA2 | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Return Path Sub-TLVs |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Return Path TLV
Return Path TLV (value TBA2) to carry one Sub-TLV for return path:
Sub-TLVs Types:
Type (value 1): Return Path Control Code. Reply test packet based on the control code flags.
  0x0: No Reply Requested.
  0x1: In-band Reply Requested.
Type (value 2): Return Address. Destination address for the reply; different than the Source Address in the test packet
Type (value 3): SR-MPLS Label Stack of the Return SR Path
Type (value 4): SR-MPLS Binding SID [draft-ietf-pce-binding-label-sid] of the Return SR Policy
Type (value 5): SRv6 Segment List of the Return SR Path
Type (value 6): SRv6 Binding SID [draft-ietf-pce-binding-label-sid] of the Return SR Policy
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|STAMP TLV Flags| Type | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(1) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
. .
. .
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Segment(n) |
. .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Figure: Segment List Sub-TLV in Return Path TLV

## Slide 6: Return Path Control Code Sub-TLV - Usage
In-band Reply:
  For link delay measurement
    Session-Reflector sends reply on the same incoming link in the reverse direction
    Link can be Virtual, LAG or LAG member
  Avoid provisioning each test session (session id, source-address) on Session-Reflector (can have an order of 1K links)
    Stateless mode of STAMP Session-Reflector as defined in RFC 8762
No Reply:
  The Session-Reflector does not transmit reply test packet back to the Session-Sender and terminates the test session
  The Session-Reflector sends performance metrics via streaming telemetry using the information from the received test packet

## Slide 7: Return Address Sub-TLV - Usage
The STAMP reply test packet may be transmitted to a different node than the Session-Sender
  e.g. to a controller for telemetry use-cases.
For this, the Session-Sender can specify in the test packet the receiving destination address for the Session-Reflector reply test packet.

## Slide 8: Return Path Segment List Sub-TLVs - Usage
For SR path, reply test packet may need to be sent on a specific return SR path
Bidirectional SR path (forward and reverse) dynamically computed using CSPF by the head-end node
  Path can change often based on topology change, link/node failure in the network, etc.
No signaling in SR (PCE can be used)
Avoid signaling and maintaining dynamic state on Session-Reflector to store return paths for each test session (each session-id, source-address)
  Order of 10K SR Policy (that can have active and standby candidate-path and each can have multiple segment-lists)

## Slide 9: Next Steps
Welcome your comments and suggestions
Requesting WG adoption

## Slide 10
Thank you